## Slide 1
UNIVERSITY OF CLAUDE
UC LINA 600 — Linear Algebra for Graphics
MODULE 08
The Pipeline as a Matrix Chain
Where the course pays off, visibly.
UC LINA 600 · Module 08 of 13 · original material, share freely

## Slide 2
MODULE OUTCOMES
What you will be able to do
▪ Derive the model and view matrices.
▪ Derive a perspective projection matrix.
▪ Explain the depth mapping and its precision problem.
▪ Explain the viewport transform.
▪ Assemble and verify the full chain.
UC LINA 600 · Linear Algebra for Graphics — Module 08
1
Notes: State the outcomes before the content. Every slide that follows exists to serve one of these.

## Slide 3
PART 1
Model and view
Both of which you can now build.
UC LINA 600 · Linear Algebra for Graphics — Module 08
2

## Slide 4
The model matrix composes the object's transforms and the view matrix is the camera frame inverted
TWO MATRICES, BOTH ALREADY DERIVED
Model: scale, then rotate, then translate — composed right to left as TRS, which is the conventional order and gives the behaviour people expect (Module 03 §2).
And the order matters visibly: rotating after translating orbits the object around the origin, which is sometimes what you want and is usually a bug.
View: build the camera's orthonormal frame and invert it (Module 04 §3) — which is a transpose plus a negated translation, and is four lines.
So two of the four matrices are already yours, from Modules 03 and 04 — and the projection is the only new one.
UC LINA 600 · Linear Algebra for Graphics — Module 08
3

## Slide 5
PART 2
Deriving the projection
From similar triangles, in four lines.
UC LINA 600 · Linear Algebra for Graphics — Module 08
4

## Slide 6
PROJECTION
Where the matrix comes from
text
THE GEOMETRY: a point at depth z projects onto a
screen plane at distance d by similar triangles:
x_screen = d * x / (-z) (z negative,
y_screen = d * y / (-z) camera looks -z)
THAT IS A DIVISION, so we need w (Module 07):
arrange for w = -z and let the hardware divide.
[ d 0 0 0 ] so x' = d*x
[ 0 d 0 0 ] y' = d*y
[ 0 0 A B ] z' = A*z + B
[ 0 0 -1 0 ] w' = -z
after the divide: x'/w' = -d*x/z. Correct.
AND A, B ARE CHOSEN to map the near and far planes
to the depth range the hardware wants:
z = -n -> z'/w' = -1 (or 0)
z = -f -> z'/w' = +1
two equations, two unknowns, and you solve them.
THAT IS THE WHOLE DERIVATION.
Similar triangles, one row to put depth in w, and two equations for the depth range — which is the whole projection matrix.
UC LINA 600 · Linear Algebra for Graphics — Module 08
5
Notes: Project 2 requires this derived rather than copied.

## Slide 7
PART 3
Depth precision
Which follows from the derivation and surprises people.
UC LINA 600 · Linear Algebra for Graphics — Module 08
6

## Slide 8
Depth after the divide is non-linear in z, so almost all the precision sits near the near plane
THE CONSEQUENCE OF THE A AND B ROW
z' / w' works out to something of the form a + b/z — a reciprocal — so equal steps in stored depth are not equal steps in distance.
Which means a near plane at 0.01 and a far plane at 10,000 spends most of its depth buffer on the first metre — and the rest of the scene fights over what is left.
That is z-fighting: two distant surfaces rounding to the same depth value and flickering — and the fix is almost always to move the near plane out, not the far plane in.
Which is a specific, common, and frequently misdiagnosed bug — and it falls directly out of Part 2's derivation, which is why deriving rather than copying matters.
UC LINA 600 · Linear Algebra for Graphics — Module 08
7

## Slide 9
PART 4
Assembling and checking
The chain, and how to know it is right.
UC LINA 600 · Linear Algebra for Graphics — Module 08
8

## Slide 10
ASSEMBLY
The full chain, and the checks at each stage
▪ p_clip = Projection · View · Model · p_model — right to left, and the naming convention makes the composition checkable (Module 04 §2).
▪ Then the divide by w, giving normalised device coordinates in a cube — and anything outside that cube is clipped.
▪ Then the viewport transform: scale and shift the cube to pixel coordinates, which is a trivial affine map and is where the y-flip usually hides.
▪ And check each stage separately: a point you computed by hand, at every stage, rather than looking at the final image (Module 13 §2).
▪ Which is the only way to localise an error in a chain of four — the image tells you something is wrong and never which matrix.
The image tells you something is wrong and never which matrix — so check each stage against a hand-computed point.
UC LINA 600 · Linear Algebra for Graphics — Module 08
9

## Slide 11
And the course's payoff is here
CLOSING
Everything in Modules 02 through 07 was for this — bases, change of basis, linearity, and homogeneous coordinates, all four used in one derivation.
And the derivation is about twenty lines total — which is why the course is four weeks rather than a semester, and why skipping it costs more than it saves.
Plus: you can now debug it, which was Module 01 §1's whole argument — a copied matrix gives a picture and a derived one gives a diagnosis.
So Project 2 asks for the derivations alongside the renderer — because the renderer alone does not demonstrate the thing the course was for.
UC LINA 600 · Linear Algebra for Graphics — Module 08
10

## Slide 12
What to carry forward
1. Model is TRS composed right to left; rotating after translating orbits the origin, which is usually a bug.
2. The view matrix is the camera frame inverted — a transpose plus a negated translation.
3. The projection matrix is similar triangles, one row to put depth in w, and two equations for the depth range.
4. Depth after the divide is a reciprocal in z, so almost all precision sits near the near plane.
5. Z-fighting is fixed by moving the near plane out, not the far plane in.
6. The image tells you something is wrong and never which matrix, so check each stage against a hand-computed point.
UC LINA 600 · Linear Algebra for Graphics — Module 08
11