## Slide 1
UNIVERSITY OF CLAUDE
CSCE 611 — Operating Systems
MODULE 10
I/O and Device Drivers
Talking to hardware that is slow, asynchronous, and hostile.
CSCE 611 · Module 10 of 13 · original material, share freely

## Slide 2
MODULE OUTCOMES
What you will be able to do
▪ Explain memory-mapped I/O and port I/O.
▪ Compare polling and interrupts and say when each is right.
▪ Explain DMA and why it matters.
▪ Explain the top-half/bottom-half split in interrupt handling.
▪ Explain the block layer and I/O scheduling.
CSCE 611 · Operating Systems — Module 10
1
Notes: State the outcomes before the content. Every slide that follows exists to serve one of these.

## Slide 3
PART 1
Talking to a device
Registers that are not memory.
CSCE 611 · Operating Systems — Module 10
2

## Slide 4
TWO MECHANISMS
How the CPU reaches a device
Memory-mapped I/O
▪ Device registers appear at physical addresses.
▪ Read and write them with ordinary loads and stores.
▪ Must be marked uncacheable — or the cache will serve stale values and swallow writes.
  – Also needs volatile and barriers.
▪ What everything modern uses.
Port I/O
▪ A separate address space with dedicated instructions.
▪ in and out on x86.
▪ No cache interaction by construction.
  – Legacy; x86 only.
▪ Still used for a few ancient devices.
CSCE 611 · Operating Systems — Module 10
3
Notes: The uncacheable requirement is a real bug source: a driver that works and then fails after a cache config change.

## Slide 5
Device registers are not memory
THE TRAP
Reading a status register can have side effects — it may clear an interrupt, or pop a value from a FIFO.
Writing the same value twice is not the same as writing it once.
So the compiler must not cache the value in a register, must not reorder accesses, and must not eliminate 'redundant' reads. That is what volatile is actually for — this, not thread synchronisation (CSCE 614 Module 12).
And the processor must not reorder either, which needs explicit memory barriers.
CSCE 611 · Operating Systems — Module 10
4

## Slide 6
PART 2
Knowing when the device is ready
Ask repeatedly, or be told.
CSCE 611 · Operating Systems — Module 10
5

## Slide 7
NOTIFICATION
Polling and interrupts
Polling
Interrupts
Mechanism
Read a status register in a loop
The device raises a signal
CPU cost while waiting
100%
Zero
Latency
Very low
Interrupt entry overhead
Good for
Fast devices; very high rates
Slow or infrequent devices
Example
NVMe at high queue depth; NIC under load
Keyboard, disk completion
CSCE 611 · Operating Systems — Module 10
6
Notes: The modern twist: for very fast devices, polling wins again. NAPI and NVMe poll mode exist for exactly this.

## Slide 8
At high rates, interrupts become the problem
INTERRUPT LIVELOCK
A network card at ten million packets per second generates ten million interrupts per second. Each costs context save, handler entry, and a cache disturbance.
The system spends all its time entering and leaving interrupt handlers and never runs the code that would process the packets. Throughput collapses while the CPU is fully busy — this is interrupt livelock.
Fix: on the first interrupt, disable interrupts for that device and switch to polling. Re-enable when the queue drains.
Linux's NAPI does exactly this. Interrupts for low rates, polling for high — adaptively.
CSCE 611 · Operating Systems — Module 10
7

## Slide 9
PART 3
DMA
Letting the device move the data.
CSCE 611 · Operating Systems — Module 10
8

## Slide 10
DMA
Why programmed I/O does not scale
▪ Programmed I/O: the CPU copies every byte between the device and memory.
  – A 1 GB/s device would consume a core entirely, doing nothing but copying.
▪ DMA: give the device a buffer address and a length. It writes memory directly and interrupts when finished.
▪ The CPU is free during the transfer. This is why high-throughput I/O is possible at all.
▪ Cost: the device now writes memory behind the CPU's back.
CSCE 611 · Operating Systems — Module 10
9
Notes: The coherence consequence on the next slide is the part driver authors must get right.

## Slide 11
DMA and cache coherence
WHERE DRIVERS GO WRONG
The device writes physical memory directly. The CPU's cache does not know.
Before a device read: flush the buffer from cache, or the device may read stale data that is still dirty in cache.
After a device write: invalidate the buffer, or the CPU may read a stale cached copy instead of the new data.
Many systems have coherent DMA where hardware handles this. Many embedded systems do not, and the resulting bugs are intermittent and look like corruption.
An IOMMU adds address translation for devices, which also makes DMA safe to expose to a virtual machine.
CSCE 611 · Operating Systems — Module 10
10

## Slide 12
PART 4
Interrupt handlers
Do the minimum now, the rest later.
CSCE 611 · Operating Systems — Module 10
11

## Slide 13
TOP AND BOTTOM HALF
Splitting the work
c
// TOP HALF -- runs with interrupts disabled. Must be FAST.
void disk_intr(void) {
ack_device(); // tell the device we heard it
struct buf *b = dequeue_completed();
b->flags |= B_VALID;
schedule_bottom_half(b); // defer everything else
}
// BOTTOM HALF -- runs later, interrupts enabled, may sleep.
void disk_bh(struct buf *b) {
wakeup(b); // wake the waiting process
update_statistics();
maybe_issue_next_request();
}
// Why: a long top half blocks ALL interrupts, including the timer.
// Miss enough timer ticks and the clock drifts and scheduling stops.
The top half acknowledges and records; everything else is deferred. Linux calls the deferred part softirqs, tasklets, or workqueues.
CSCE 611 · Operating Systems — Module 10
12
Notes: The 'missed timer ticks' consequence makes the rule concrete rather than arbitrary.

## Slide 14
BLOCK LAYER
Scheduling I/O
▪ Requests are queued, merged, and reordered before reaching the device.
▪ Merging: adjacent requests become one — a large win.
▪ Reordering: on spinning disks, elevator ordering minimised seek time.
  – On SSDs there is no seek, so this matters far less — and the schedulers changed accordingly.
▪ Modern NVMe: many deep queues, one per core. none is often the best scheduler, because the device schedules better than the kernel can.
A case where the right answer reversed when the hardware changed.
CSCE 611 · Operating Systems — Module 10
13

## Slide 15
What to carry forward
1. Device registers are not memory: reads have side effects, so accesses need volatile, barriers, and uncacheable mappings.
2. Polling burns CPU and has low latency; interrupts are free while waiting and cost entry overhead. Fast devices have swung the answer back to polling.
3. At very high event rates, interrupts cause livelock. NAPI switches to polling adaptively.
4. DMA lets the device move data directly, which is why high-throughput I/O is possible — and it creates cache coherence obligations.
5. Split handlers: the top half acknowledges and records with interrupts off; everything else is deferred to a bottom half that may sleep.
6. I/O scheduling mattered enormously for seek time and matters far less for SSDs. The right answer changed when the hardware did.
CSCE 611 · Operating Systems — Module 10
14