## Slide 1
UNIVERSITY OF CLAUDE
CSCE 614 — Computer Architecture
MODULE 02
Instruction Sets and the Hardware/Software Interface
The contract between the compiler and the chip.
CSCE 614 · Module 02 of 13 · original material, share freely

## Slide 2
MODULE OUTCOMES
What you will be able to do
▪ Explain what an ISA specifies and what it deliberately leaves open.
▪ Compare RISC and CISC design philosophies and their modern convergence.
▪ Read compiler-generated assembly well enough to diagnose performance.
▪ Explain addressing modes and the cost of each.
▪ Explain why the ISA is an abstraction boundary, and why that matters.
CSCE 614 · Computer Architecture — Module 02
1
Notes: State the outcomes before the content. Every slide that follows exists to serve one of these.

## Slide 3
PART 1
What an ISA is
A contract, deliberately silent about implementation.
CSCE 614 · Computer Architecture — Module 02
2

## Slide 4
THE CONTRACT
Specified, and deliberately not
The ISA specifies
▪ The instructions and what each one does.
▪ Registers: how many, how wide.
▪ Memory addressing modes.
▪ Data types and their representations.
▪ Exception and interrupt behaviour.
  – Everything software can observe.
The ISA says nothing about
▪ Pipeline depth.
▪ Cache sizes or organisation.
▪ Whether execution is in order.
▪ Branch prediction.
▪ How many instructions issue per cycle.
  – Everything this course is about.
CSCE 614 · Computer Architecture — Module 02
3
Notes: The right column is the whole point: it is what lets one ISA survive thirty years of radically different implementations.

## Slide 5
The ISA is why x86 is still here
WHY THE BOUNDARY MATTERS
A 1985 program still runs on a 2026 processor, despite the two sharing essentially no implementation.
The 2026 chip decodes those instructions into internal micro-operations, reorders them, executes them speculatively on a dozen functional units, and retires them in order to maintain the illusion of sequential execution.
The ISA is the only thing held constant. Everything beneath it has been free to change completely, and has.
This is an abstraction boundary doing an enormous amount of economic work — and like all abstraction boundaries, it leaks exactly where performance is concerned.
CSCE 614 · Computer Architecture — Module 02
4

## Slide 6
PART 2
RISC and CISC
An old argument whose resolution is more interesting than either side.
CSCE 614 · Computer Architecture — Module 02
5

## Slide 7
PHILOSOPHIES
The original positions
CISC (x86, VAX)
RISC (ARM, RISC-V, MIPS)
Instructions
Many, complex, variable length
Few, simple, fixed length
Memory access
Most instructions may touch memory
Only load and store
Registers
Few (8 in 32-bit x86)
Many (32 typical)
Decoding
Hard — variable length
Easy — fixed width
Rationale
Small code; compilers were weak
Simple hardware; pipelines cleanly
CSCE 614 · Computer Architecture — Module 02
6
Notes: The historical context matters: CISC made sense when memory was expensive and compilers were poor. Both changed.

## Slide 8
How the argument actually resolved
THE INTERESTING PART
Modern x86 decodes its complex instructions into simple internal micro-operations and executes those on a RISC-like core. The CISC instruction set survives as a compatibility interface, not as an implementation strategy.
Meanwhile ARM and RISC-V have accumulated vector extensions, cryptography instructions, and other complex operations where they pay.
So RISC won the argument about how to build a processor, and CISC won the market through compatibility. Both outcomes are real, and the apparent contradiction dissolves once you see the ISA as an interface rather than a design.
CSCE 614 · Computer Architecture — Module 02
7

## Slide 9
PART 3
Reading assembly
You do not need to write it. You do need to read it.
CSCE 614 · Computer Architecture — Module 02
8

## Slide 10
WHY READ IT
The compiler is doing more than you think
asm
// C source: int sum(int* a, int n) {
// int s = 0;
// for (int i = 0; i < n; i++) s += a[i];
// return s;
// }
// x86-64 at -O3, abbreviated:
sum:
test esi, esi ; n == 0?
jle .empty
...
.vector_loop:
vpaddd ymm0, ymm0, [rdi+rax*4] ; EIGHT ints added per
vpaddd ymm1, ymm1, [rdi+rax*4+32] ; instruction, two
add rax, 16 ; accumulators to break
cmp rax, rdx ; the dependency chain
jb .vector_loop
... ; horizontal sum, then a
; scalar tail for leftovers
The compiler vectorised the loop, unrolled it, used two accumulators to break the dependency chain, and generated a scalar tail. None of that is visible in the C.
CSCE 614 · Computer Architecture — Module 02
9
Notes: Compiler Explorer is the single most useful tool introduced in this course. Get them using it in week two.

## Slide 11
WHAT TO LOOK FOR
Reading assembly for performance
▪ Did it vectorise? Look for ymm/zmm registers and v-prefixed instructions.
▪ Did it unroll? Repeated instruction groups per iteration.
▪ Is the loop body tight? Spills to stack memory mean register pressure.
▪ Are there branches inside? Could they be made branchless (Module 04)?
▪ Is there a division? 20–40 cycles; often replaceable.
▪ Function calls in the loop? Not inlined means the compiler could not see enough.
You are not checking the compiler's work. You are finding out what it could not prove.
CSCE 614 · Computer Architecture — Module 02
10

## Slide 12
ADDRESSING
Addressing modes and their cost
Mode
Example
Cost
Register
add rax, rbx
Free
Immediate
add rax, 42
Free
Base + displacement
mov rax, [rbp-8]
One memory access
Base + index×scale
mov rax, [rdi+rsi*8]
Same — computed in the AGU
Indirect through pointer
mov rax, [rax]
Same, but serialised
CSCE 614 · Computer Architecture — Module 02
11
Notes: The last row is the important one: pointer chasing is not more expensive per access, it is less parallel, and that is worse.

## Slide 13
Why pointer chasing is slow
THE THING TO REMEMBER
Address arithmetic is free — dedicated address generation units compute base + index×scale + displacement at no cost.
What is expensive is a dependent load: p = p->next cannot begin until the previous load has returned. Each access serialises on the one before it.
An array scan issues many independent loads that overlap, so the memory system works on several at once. A linked list issues one at a time and waits ~250 cycles for each.
This is why the two data structures differ by 10–50× despite identical asymptotics — the point CSCE 629 Module 01 could only assert.
CSCE 614 · Computer Architecture — Module 02
12

## Slide 14
PERSPECTIVE
The ISA as a leaky abstraction
▪ The ISA promises what instructions do, not how fast.
▪ So two programs that are functionally identical can differ by 50× and both be correct ISA-level code.
▪ Performance lives entirely in the part the ISA does not specify.
  – Which is why you cannot reason about speed from the instruction set alone.
  – And why the remaining eleven modules exist.
▪ Speculative execution vulnerabilities (Spectre) were this abstraction leaking in a security-relevant direction.
CSCE 614 · Computer Architecture — Module 02
13
Notes: The Spectre point lands well: the abstraction boundary was always leaky for performance, and it turned out to leak for confidentiality too.

## Slide 15
What to carry forward
1. An ISA specifies what software can observe and deliberately says nothing about pipeline, caches, or execution order — which is exactly what lets implementations change radically.
2. RISC won the argument about how to build processors; CISC won the market through compatibility. Modern x86 decodes to RISC-like micro-operations.
3. Read the generated assembly. The compiler vectorises, unrolls, and breaks dependency chains in ways invisible in the source.
4. Address arithmetic is free; dependent loads are not. Pointer chasing is slow because it serialises, not because each access costs more.
5. That serialisation is why arrays beat linked lists by 10–50× at identical asymptotic complexity.
6. Performance lives entirely in what the ISA does not specify — which is the subject of the rest of this course.
CSCE 614 · Computer Architecture — Module 02
14