## Slide 1
UNIVERSITY OF CLAUDE
CSCE 614 — Computer Architecture
MODULE 03
Pipelining and Hazards
Overlapping instructions, and the three things that stop you.
CSCE 614 · Module 03 of 13 · original material, share freely

## Slide 2
MODULE OUTCOMES
What you will be able to do
▪ Explain the classic five-stage pipeline and why pipelining raises throughput, not latency.
▪ Identify structural, data, and control hazards.
▪ Explain forwarding and when it is insufficient.
▪ Explain why deeper pipelines increase misprediction cost.
▪ Relate pipeline behaviour to measurable CPI.
CSCE 614 · Computer Architecture — Module 03
1
Notes: State the outcomes before the content. Every slide that follows exists to serve one of these.

## Slide 3
PART 1
The idea
An assembly line for instructions.
CSCE 614 · Computer Architecture — Module 03
2

## Slide 4
STAGES
The classic five stages
Stage
Does
Needs
IF — fetch
Read the instruction from memory
Instruction cache, PC
ID — decode
Decode it; read registers
Register file
EX — execute
Do the arithmetic; compute addresses
ALU
MEM — memory
Load or store
Data cache
WB — write back
Write the result to a register
Register file
CSCE 614 · Computer Architecture — Module 03
3
Notes: Real pipelines are 14-20 stages, but the five-stage model exposes every concept and nothing extra.

## Slide 5
Throughput, not latency
KEY IDEA
Pipelining does not make any single instruction faster. An instruction still traverses all five stages.
It makes the processor finish one instruction per cycle instead of one every five, by overlapping five instructions in different stages.
Ideal speedup is the number of stages. In practice it is less, because of hazards — and because the pipeline registers between stages add real delay.
This is the same throughput-versus-latency distinction as the graphics pipeline in CSCE 641, and for the same reason.
CSCE 614 · Computer Architecture — Module 03
4

## Slide 6
PART 2
Three hazards
Everything that prevents the next instruction starting on schedule.
CSCE 614 · Computer Architecture — Module 03
5

## Slide 7
HAZARDS
The three classes
Hazard
Cause
Fix
Structural
Two instructions need the same hardware
Duplicate it, or stall
Data
An instruction needs a result not yet produced
Forwarding; stall if still too early
Control
The next address is not yet known
Predict and speculate (Module 04)
CSCE 614 · Computer Architecture — Module 03
6
Notes: Everything in the next ten modules is an elaboration of one of these three rows.

## Slide 8
DATA HAZARD
Forwarding: the result before it is written
asm
add r1, r2, r3 ; r1 is produced in EX, written in WB
sub r4, r1, r5 ; needs r1 in its OWN EX -- one cycle later
Without forwarding: sub must wait until add reaches WB -> 3 stalls.
With forwarding: the ALU output of `add` is routed directly to the
ALU input of `sub`. Zero stalls.
BUT:
ld r1, 0(r2) ; r1 available only after MEM
add r4, r1, r5 ; needs r1 in EX -- which is EARLIER
-> the value does not exist yet. Forwarding cannot help.
-> one unavoidable stall: the LOAD-USE HAZARD.
Forwarding removes most data hazards. The load-use case is the one it cannot, which is why compilers schedule an independent instruction into that slot.
CSCE 614 · Computer Architecture — Module 03
7
Notes: The load-use hazard is the one that survives into modern machines, and the reason instruction scheduling matters.

## Slide 9
DATA HAZARDS
Three kinds of dependence
▪ RAW (read after write) — a true dependence. Real information flow; cannot be removed.
▪ WAR (write after read) and WAW (write after write) — false dependences.
  – They exist only because two instructions happened to use the same register name.
  – Removed by register renaming — Module 08.
▪ Only RAW is fundamental. The other two are artefacts of having finitely many architectural register names.
CSCE 614 · Computer Architecture — Module 03
8
Notes: Framing WAR/WAW as naming artefacts makes register renaming feel inevitable rather than clever.

## Slide 10
Control hazards are the expensive ones
THE REAL PROBLEM
After a branch, the processor does not know which instruction to fetch next until the branch resolves in EX.
Stalling until then wastes several cycles on every single branch — and roughly one instruction in five is a branch.
That is intolerable, so processors guess and execute speculatively. When the guess is right, nothing is lost; when wrong, the speculated work is discarded.
The entire mechanism of Module 04 exists because of this one hazard.
CSCE 614 · Computer Architecture — Module 03
9

## Slide 11
PART 3
Depth and its costs
Why pipelines got deeper, and why that stopped.
CSCE 614 · Computer Architecture — Module 03
10

## Slide 12
DEPTH
Deeper pipelines: the trade
▪ Less work per stage → shorter cycle → higher clock frequency.
▪ But: misprediction penalty is proportional to depth.
  – 5 stages → ~3 cycles wasted. 20 stages → ~15–20.
▪ Pentium 4 pushed to 31 stages chasing clock speed.
  – High frequency, poor performance per cycle, and enormous power. The design was abandoned.
▪ Modern cores settle around 14–20 stages — the balance point.
An instructive case of a metric (clock speed) being optimised at the expense of the thing it was a proxy for.
CSCE 614 · Computer Architecture — Module 03
11

## Slide 13
COST
What hazards do to CPI
CPI = 1 + stalls per instruction
Ideal pipelined CPI is 1. Everything above that is a hazard.
branch stalls = frequency × misprediction rate × penalty
20% branches × 5% mispredicted × 15 cycles = 0.15 CPI.
memory stalls = miss rate × miss penalty
2% miss × 250 cycles = 5.0 CPI. Memory dominates everything.
Compare the last two lines. A 2% cache miss rate costs more than thirty times what a 5% branch misprediction rate does.
CSCE 614 · Computer Architecture — Module 03
12
Notes: This comparison is the justification for spending Modules 5-7 on memory and only one module on branches.

## Slide 14
IN PRACTICE
What this means for your code
▪ Dependency chains limit speed. A chain of dependent operations runs at one per latency, not one per cycle.
  – Use multiple accumulators to break chains — as the compiler did in Module 02.
▪ Loads early. Issue a load several instructions before the value is needed.
▪ Branches cost, but memory costs more. Check IPC and cache misses before restructuring control flow.
▪ Compilers schedule for this automatically. Your job is to not block them — usually by avoiding aliasing and keeping loops simple.
CSCE 614 · Computer Architecture — Module 03
13

## Slide 15
What to carry forward
1. Pipelining raises throughput, not latency: an instruction still takes five stages, but one completes per cycle.
2. Three hazards: structural (resource conflict), data (value not ready), control (next address unknown).
3. Forwarding removes most data hazards. The load-use hazard survives, which is why instruction scheduling matters.
4. Only RAW is a true dependence. WAR and WAW are artefacts of register naming, removed by renaming in Module 08.
5. Misprediction penalty scales with pipeline depth, which is why the 31-stage Pentium 4 failed and modern cores sit at 14–20.
6. A 2% cache miss rate costs ~5.0 CPI; a 5% branch miss rate costs ~0.15. Memory dominates.
CSCE 614 · Computer Architecture — Module 03
14