## Slide 1
UNIVERSITY OF CLAUDE
CSCE 614 — Computer Architecture
MODULE 04
Branch Prediction and Speculation
Guessing the future, and the cost of being wrong.
CSCE 614 · Module 04 of 13 · original material, share freely

## Slide 2
MODULE OUTCOMES
What you will be able to do
▪ Explain why branch prediction is necessary rather than merely helpful.
▪ Describe static, bimodal, two-level, and modern predictors.
▪ Measure the misprediction penalty on your own machine.
▪ Write branchless code and judge when it is worth it.
▪ Explain speculative execution and its security consequences.
CSCE 614 · Computer Architecture — Module 04
1
Notes: State the outcomes before the content. Every slide that follows exists to serve one of these.

## Slide 3
PART 1
Why guess at all
The arithmetic makes stalling impossible.
CSCE 614 · Computer Architecture — Module 04
2

## Slide 4
THE ARITHMETIC
Why you cannot simply stall
~20% of instructions are branches
One in five. Conditionals, loops, calls, returns.
pipeline depth ~15–20 stages
The branch resolves well after it was fetched.
stalling every branch ⇒ CPI ≈ 1 + 0.2×15 = 4
A fourfold slowdown. Completely unacceptable.
So the processor guesses, and executes speculatively. Prediction is not an optimisation — deep pipelines are impossible without it.
CSCE 614 · Computer Architecture — Module 04
3
Notes: Framing prediction as a precondition rather than a refinement is the right emphasis.

## Slide 5
SPECULATION
What speculative execution means
▪ Predict the branch outcome; fetch and execute down the predicted path immediately.
▪ Results are held provisionally — not committed to architectural state.
▪ Right: commit everything. Nothing was lost.
▪ Wrong: discard the speculated work and restart from the correct address.
  – Cost is the pipeline depth — everything in flight is thrown away.
▪ At 95% accuracy this is overwhelmingly profitable.
CSCE 614 · Computer Architecture — Module 04
4

## Slide 6
PART 2
How prediction works
From one bit to neural-inspired, in four steps.
CSCE 614 · Computer Architecture — Module 04
5

## Slide 7
PREDICTORS
The evolution
Predictor
Mechanism
Accuracy
Static
Always taken; or backward-taken, forward-not
~60–70%
1-bit
Remember the last outcome for this branch
~80%
2-bit bimodal
Saturating counter — needs two misses to flip
~85–90%
Two-level / gshare
Index by branch address XOR global history
~93–96%
TAGE / perceptron
Many history lengths, tagged, combined
~98–99%
CSCE 614 · Computer Architecture — Module 04
6
Notes: The jump from bimodal to two-level is the conceptual one: correlation between branches is real and exploitable.

## Slide 8
Why two bits rather than one
THE KEY REFINEMENT
A 1-bit predictor mispredicts twice per loop: once on the final iteration (predicts taken, loop exits) and once on the first iteration of the next execution (now predicts not-taken).
A 2-bit saturating counter requires two consecutive wrong outcomes before changing its prediction. A single anomalous outcome — like a loop exit — does not flip it.
For a loop of n iterations, mispredictions drop from 2 per execution to 1. One extra bit of state, and roughly half the misses removed. The hysteresis is the whole idea.
CSCE 614 · Computer Architecture — Module 04
7

## Slide 9
CORRELATION
Why global history helps
▪ Branches are not independent. Later ones often depend on earlier ones.
▪ if (x > 0) ... ; if (x > 10) ...
  – The second is highly predictable given the first.
▪ A two-level predictor indexes its table by branch address combined with recent global outcomes.
  – So the same branch gets different predictions in different contexts.
▪ gshare: index = PC XOR global history register. Simple, and a large accuracy gain.
CSCE 614 · Computer Architecture — Module 04
8
Notes: The correlation insight (Yeh & Patt) is one of the genuinely clever ideas in the field.

## Slide 10
ALSO PREDICTED
Direction is not the only problem
▪ Direction — taken or not. The main predictor.
▪ Target — where to, for indirect branches. The Branch Target Buffer caches recent targets.
  – Virtual calls and switch statements are indirect, and harder.
▪ Returns — a Return Address Stack, pushed on call and popped on return.
  – Almost perfectly accurate, since calls and returns nest.
▪ Deep recursion can overflow the RAS, and accuracy collapses.
Virtual dispatch costs most when the target varies unpredictably — which is exactly when polymorphism is most useful.
CSCE 614 · Computer Architecture — Module 04
9

## Slide 11
PART 3
Measuring and avoiding
What you can do about it.
CSCE 614 · Computer Architecture — Module 04
10

## Slide 12
MEASURE
The classic experiment
c
// Fill an array with random values, then branch on them.
for (i = 0; i < N; i++) a[i] = rand() % 256;
uint64_t sum = 0;
for (rep = 0; rep < 1000; rep++)
for (i = 0; i < N; i++)
if (a[i] >= 128) sum += a[i]; // ~50% taken, UNPREDICTABLE
// Now SORT the array and run the identical loop again.
sort(a, N);
// Same instruction count. Same memory access pattern.
// Typically 3-6x FASTER -- the branch is now almost always
// correctly predicted.
Identical work, identical data, identical memory traffic. The only difference is predictability. This is the single most convincing demonstration in the course.
CSCE 614 · Computer Architecture — Module 04
11
Notes: Every student should run this. It makes branch prediction real in a way no diagram does.

## Slide 13
AVOID
Branchless: pay always, never mispredict
c
// Branchy: 0 or ~15 cycles, depending on prediction
if (a[i] >= 128) sum += a[i];
// Branchless: always ~1-2 cycles, never mispredicts
sum += a[i] * (a[i] >= 128); // multiply by 0 or 1
// Or with a conditional move (often emitted automatically):
int t = (a[i] >= 128) ? a[i] : 0;
sum += t;
Worth it when the branch is unpredictable. A loss when the branch predicts well, because you pay the work on every iteration instead of almost never.
CSCE 614 · Computer Architecture — Module 04
12
Notes: The trade is the point: branchless is not strictly better, it is a different risk profile.

## Slide 14
JUDGEMENT
When to go branchless
Situation
Verdict
Branch is data-dependent and ~50/50
Yes — the big win
Branch is almost always one way
No — prediction is already free
Both sides are cheap
Probably yes
One side is expensive
No — you would always pay it
Inside a hot inner loop
Measure. Do not guess.
CSCE 614 · Computer Architecture — Module 04
13

## Slide 15
Spectre: speculation leaks
SECURITY
Mis-speculated instructions are discarded architecturally — but they ran, and they left data in the cache.
An attacker can induce speculation past a bounds check, cause a secret-dependent memory access, and then recover the secret by timing cache accesses. The architectural state was never wrong; the microarchitectural state carried the information out.
The ISA guaranteed no architectural effect, and that guarantee held. It said nothing about timing, and timing was enough.
Mitigations cost real performance. This is the Module 02 abstraction leak, in a form nobody designed for.
CSCE 614 · Computer Architecture — Module 04
14

## Slide 16
What to carry forward
1. With 20% branches and a 15-stage pipeline, stalling on every branch gives CPI 4. Prediction is a precondition for deep pipelines, not an optimisation.
2. A 2-bit saturating counter needs two consecutive misses to change its mind, which halves loop mispredictions compared with 1 bit.
3. Branches correlate. Two-level predictors index by address combined with global history, reaching 95%+; TAGE reaches 98–99%.
4. Direction, target, and return address are predicted by separate mechanisms. Indirect calls are the hard case.
5. Sorting an array makes an identical loop 3–6× faster purely by making one branch predictable.
6. Branchless code is worth it only when the branch is genuinely unpredictable and both sides are cheap. Otherwise it is a loss.
CSCE 614 · Computer Architecture — Module 04
15