## Slide 1
UNIVERSITY OF CLAUDE
CSCE 614 — Computer Architecture
MODULE 05
Caches: The Memory Wall
The gap that shapes every modern machine.
CSCE 614 · Module 05 of 13 · original material, share freely

## Slide 2
MODULE OUTCOMES
What you will be able to do
▪ Explain the memory wall and its historical origin.
▪ Explain temporal and spatial locality and why caches work at all.
▪ Analyse direct-mapped, set-associative, and fully associative caches.
▪ Classify misses as compulsory, capacity, or conflict.
▪ Measure your own machine's cache hierarchy.
CSCE 614 · Computer Architecture — Module 05
1
Notes: State the outcomes before the content. Every slide that follows exists to serve one of these.

## Slide 3
PART 1
The wall
Two exponential curves with different exponents.
CSCE 614 · Computer Architecture — Module 05
2

## Slide 4
The memory wall
THE ORGANISING FACT
From roughly 1980 to 2005, processor speed improved about 50% per year. DRAM latency improved about 7% per year.
Compounded over twenty-five years, the gap grew by more than two orders of magnitude. An access that once cost a few cycles now costs two to three hundred.
DRAM bandwidth has improved far more than latency — you can get a great deal of data, but the first byte still takes a long time to arrive.
Essentially every architectural mechanism from here on exists to avoid that latency or to find other work to do during it.
CSCE 614 · Computer Architecture — Module 05
3

## Slide 5
HIERARCHY
A typical modern hierarchy
Level
Size
Latency
Notes
Registers
~1 KB
0
Named by the ISA
L1 data
32–48 KB
~4 cyc
Per core; split from L1 instruction
L2
0.5–2 MB
~12 cyc
Per core, usually
L3
8–64 MB
~40 cyc
Shared across cores
DRAM
8–128 GB
~250 cyc
Shared, and far away
SSD
0.5–4 TB
~10⁵ cyc
A different world
CSCE 614 · Computer Architecture — Module 05
4
Notes: Each level is roughly 10x bigger and 3-5x slower than the one above. That geometric structure is not an accident.

## Slide 6
WHY IT WORKS
Locality is the whole justification
▪ A cache only helps if future accesses are predictable from past ones. Real programs oblige.
▪ Temporal locality — a recently used item is likely to be used again.
  – Loop variables, hot functions, frequently traversed structures.
▪ Spatial locality — items near a used item are likely to be used soon.
  – Array traversal, struct fields, sequential instruction fetch.
▪ Caches exploit temporal locality by keeping and spatial locality by fetching a whole line.
CSCE 614 · Computer Architecture — Module 05
5
Notes: Spatial locality is why the cache line exists, and the line is the unit everything else is measured in.

## Slide 7
PART 2
Organisation
Where can a line live, and how do you find it?
CSCE 614 · Computer Architecture — Module 05
6

## Slide 8
PLACEMENT
Three placement policies
Policy
A line may live
Lookup
Problem
Direct-mapped
In exactly one set
One tag compare
Conflict misses
N-way set associative
In any of N ways of one set
N compares
Cost of N
Fully associative
Anywhere
Compare all
Impractical above tiny sizes
CSCE 614 · Computer Architecture — Module 05
7
Notes: 8-way is the common compromise for L1. The TLB is often fully associative because it is small.

## Slide 9
ADDRESSING
How an address is split
text
63 12 11 6 5 0
+-----------------------------+-----------+----------+
| TAG | INDEX | OFFSET |
+-----------------------------+-----------+----------+
OFFSET which byte within the cache line (64B line -> 6 bits)
INDEX which set to look in (64 sets -> 6 bits)
TAG compared against stored tags to confirm a hit
A 32 KB, 8-way, 64-byte-line cache:
32768 / 64 = 512 lines
512 / 8 ways = 64 sets -> 6 index bits
NOTE: the index comes from the MIDDLE bits, not the top.
Sequential addresses therefore spread across sets rather than
all landing in one -- which is the point.
The middle-bit indexing is deliberate. Using the top bits would map an entire contiguous array to a single set.
CSCE 614 · Computer Architecture — Module 05
8
Notes: Students rarely ask why the index is in the middle. Telling them makes the conflict-miss discussion land.

## Slide 10
PART 3
Misses
Three causes, and a different fix for each.
CSCE 614 · Computer Architecture — Module 05
9

## Slide 11
THE THREE CS
Classify before you optimise
Miss type
Cause
Fix
Compulsory
First ever reference to this line
Prefetching; larger lines
Capacity
Working set exceeds the cache
Blocking/tiling; shrink the data
Conflict
Too many lines map to one set
Padding; change the stride; more associativity
CSCE 614 · Computer Architecture — Module 05
10
Notes: Conflict misses are the surprising ones: plenty of free cache, and still missing. Always suspect a power-of-two stride.

## Slide 12
Why power-of-two strides are dangerous
THE CLASSIC TRAP
The set index comes from middle address bits. A stride that is a large power of two leaves those bits unchanged, so every access lands in the same set.
Walking a column of a 1024×1024 float matrix strides by 4096 bytes. With 64 sets of 64-byte lines, every element maps to the same set. An 8-way cache holds 8 of them; the ninth evicts the first.
You now miss on every access while using 8 lines out of 512. The cache is 98% empty and useless.
Fix: pad the row length to a non-power-of-two — 1024 → 1032 floats. A few kilobytes of waste for a large speedup.
CSCE 614 · Computer Architecture — Module 05
11

## Slide 13
MEASURE
Finding your cache sizes by pointer chase
c
// Build a pointer chain within a working set of `size` bytes,
// in RANDOM order so the prefetcher cannot help.
// Then time a long traversal.
for (size = 4*KB; size <= 256*MB; size *= 2) {
build_random_chain(buf, size);
t = time_chase(buf, ITERATIONS);
printf("%8zu KB %6.1f cycles/access\n", size/1024, t);
}
// Output shows PLATEAUS with sharp steps between them:
// 32 KB 4.2 <- fits in L1
// 64 KB 12.1 <- spilled to L2
// 512 KB 13.0
// 2 MB 41.5 <- spilled to L3
// 32 MB 198.0 <- spilled to DRAM
//
// Each step marks a cache capacity. You just measured the
// hierarchy without reading a datasheet.
Random order is essential — a sequential chase is perfectly prefetched and shows no steps at all.
CSCE 614 · Computer Architecture — Module 05
12
Notes: This is Project 1's core experiment and the most satisfying measurement in the course.

## Slide 14
POLICY
Replacement and writes
▪ Replacement: LRU is the ideal; true LRU is expensive above 2-way.
  – Real caches use pseudo-LRU, or tree-LRU, or random for high associativity.
▪ Write-through — write to cache and memory together. Simple; high bandwidth.
▪ Write-back — write to cache, mark dirty, write out on eviction. Standard.
▪ Write-allocate — a write miss fetches the line first.
  – Which is why writing a large array you never read still consumes read bandwidth — unless you use non-temporal stores.
Non-temporal stores bypass the cache. Useful for streaming output you will not re-read.
CSCE 614 · Computer Architecture — Module 05
13

## Slide 15
What to carry forward
1. Processors improved ~50% per year and DRAM latency ~7%. The resulting memory wall shapes every modern design.
2. Caches work only because of temporal and spatial locality. Keeping exploits the first; fetching a whole line exploits the second.
3. The set index comes from middle address bits, so sequential data spreads across sets — and power-of-two strides collapse onto one.
4. Three Cs: compulsory, capacity, conflict. Classify before optimising, because each has a different fix.
5. A power-of-two row length in a 2D array can make a cache 98% useless. Padding fixes it for a few kilobytes.
6. A random pointer chase across working-set sizes reveals your entire cache hierarchy as plateaus with sharp steps.
CSCE 614 · Computer Architecture — Module 05
14