## Slide 1
UNIVERSITY OF CLAUDE
CSCE 614 — Computer Architecture
MODULE 06
Cache Optimization and Prefetching
Restructuring code and data so the hierarchy works for you.
CSCE 614 · Module 06 of 13 · original material, share freely

## Slide 2
MODULE OUTCOMES
What you will be able to do
▪ Apply loop interchange, blocking, and fusion for locality.
▪ Choose between array-of-structs and struct-of-arrays.
▪ Explain hardware prefetching and what defeats it.
▪ Use software prefetch intrinsics and know when not to.
▪ Predict a transformation's benefit before measuring it.
CSCE 614 · Computer Architecture — Module 06
1
Notes: State the outcomes before the content. Every slide that follows exists to serve one of these.

## Slide 3
PART 1
Loop transformations
Same operations, different order, very different speed.
CSCE 614 · Computer Architecture — Module 06
2

## Slide 4
INTERCHANGE
Loop order decides everything
c
// BAD: strides by N*sizeof(float) -- one useful float per 64B line
for (j = 0; j < N; j++)
for (i = 0; i < N; i++)
sum += a[i][j];
// GOOD: strides by 4 bytes -- 16 useful floats per line
for (i = 0; i < N; i++)
for (j = 0; j < N; j++)
sum += a[i][j];
// Identical arithmetic. Identical result. Typically 5-10x faster.
The bad version fetches a 64-byte line and uses 4 bytes of it. 16× the memory traffic for the same work.
CSCE 614 · Computer Architecture — Module 06
3
Notes: Have them predict the ratio from line size before measuring. The prediction is usually close, which builds confidence in the model.

## Slide 5
BLOCKING
Tiling for the cache
c
// Naive matrix multiply: B is traversed column-wise N times.
for (i...) for (j...) for (k...) c[i][j] += a[i][k] * b[k][j];
// Blocked: work on tiles small enough to stay resident.
for (ii = 0; ii < N; ii += B)
for (jj = 0; jj < N; jj += B)
for (kk = 0; kk < N; kk += B)
for (i = ii; i < ii+B; i++)
for (j = jj; j < jj+B; j++) {
float s = c[i][j];
for (k = kk; k < kk+B; k++) s += a[i][k] * b[k][j];
c[i][j] = s;
}
// Choose B so that three B x B tiles fit in L1:
// 3 * B^2 * 4 bytes < 32 KB -> B ~ 50, so B = 32 or 48.
Each tile is loaded once and reused B times. Misses drop by roughly a factor of B.
CSCE 614 · Computer Architecture — Module 06
4
Notes: The sizing calculation is the point: blocking is not magic, it is arithmetic against a known cache size.

## Slide 6
TRANSFORMATIONS
The standard set
Transformation
Does
Helps when
Interchange
Reorder nested loops
Access stride is wrong
Blocking / tiling
Work on sub-blocks
Working set exceeds cache
Fusion
Merge loops over the same data
Data re-read between loops
Fission
Split one loop into several
Too many streams at once
Unrolling
Fewer iterations, bigger body
Loop overhead dominates
CSCE 614 · Computer Architecture — Module 06
5
Notes: Fusion and fission oppose each other. Which one helps depends on whether you are limited by reuse or by stream count.

## Slide 7
PART 2
Data layout
Often a larger win than any loop transformation.
CSCE 614 · Computer Architecture — Module 06
6

## Slide 8
AOS VS SOA
The layout decision
c
// ARRAY OF STRUCTS -- natural, and often wrong for bulk processing
struct Particle { float x,y,z, vx,vy,vz; int id; float mass; };
Particle p[N]; // 32 bytes each
for (i...) p[i].x += p[i].vx * dt; // uses 8 of every 32 bytes
// -> 75% of fetched data wasted
// STRUCT OF ARRAYS -- awkward, and what the hardware wants
struct Particles {
float x[N], y[N], z[N], vx[N], vy[N], vz[N];
};
for (i...) P.x[i] += P.vx[i] * dt; // two dense streams
// -> every byte used, and it
// vectorises cleanly
AoS is better when you touch most fields of one object. SoA is better when you touch one field of many objects — which is what bulk processing does.
CSCE 614 · Computer Architecture — Module 06
7
Notes: This is the single most valuable slide for a graphics student. Particle systems, vertex data, and ECS designs all turn on it.

## Slide 9
LAYOUT
Other layout wins
▪ Hot/cold splitting. Separate frequently accessed fields from rarely accessed ones.
  – More hot objects per cache line.
▪ Alignment. Align hot structures to 64 bytes so they do not straddle two lines.
▪ Shrink the data. float instead of double; 16-bit indices; quantised normals.
  – Half the bytes is often close to half the time when memory-bound.
▪ Avoid pointer chasing. Flat arrays with indices beat node graphs (Module 02).
CSCE 614 · Computer Architecture — Module 06
8

## Slide 10
PART 3
Prefetching
Fetching before you ask — and what stops it.
CSCE 614 · Computer Architecture — Module 06
9

## Slide 11
HARDWARE
What the prefetcher does for free
▪ Hardware detects access patterns and fetches ahead automatically.
▪ Detected easily: sequential forward, sequential backward, constant stride.
▪ Not detected: random access, pointer chasing, indirect a[b[i]].
▪ A stream that is prefetched well turns a latency problem into a bandwidth problem — and bandwidth is plentiful.
▪ Prefetchers stop at page boundaries — they cannot risk faulting on an unmapped page.
  – Which is one argument for huge pages (Module 07).
CSCE 614 · Computer Architecture — Module 06
10
Notes: The latency-to-bandwidth conversion is the key framing, and it explains why sequential access is so much faster than its latency numbers suggest.

## Slide 12
SOFTWARE
Explicit prefetch, used sparingly
c
for (i = 0; i < N; i++) {
// Ask for data ~8 iterations ahead. The distance must be tuned:
// too short and it has not arrived; too long and it is evicted
// before use.
__builtin_prefetch(&data[index[i + 8]], 0, 1);
process(data[index[i]]); // indirect: hardware CANNOT predict this
}
Worth trying for indirect access, graph traversal, and hash probing. Almost never worth it for sequential access — the hardware already does it better.
CSCE 614 · Computer Architecture — Module 06
11
Notes: Emphasise 'measure': software prefetch frequently makes things slower by adding instructions and polluting the cache.

## Slide 13
METHOD
An optimisation checklist, in order
Step
Ask
Tool
1
Is it actually memory-bound?
IPC and cache-miss counters
2
Which level is missing?
L1/L2/LLC miss counters
3
Which of the three Cs?
Vary size and stride
4
Fix layout first
AoS→SoA, hot/cold, shrink
5
Then loop structure
Interchange, block, fuse
6
Then prefetch
Only for indirect patterns
CSCE 614 · Computer Architecture — Module 06
12
Notes: The ordering matters and is frequently got backwards — people tile first and then discover SoA would have sufficed.

## Slide 14
What to carry forward
1. Loop interchange can give 5–10× with identical arithmetic, because the wrong stride wastes 15 of every 16 bytes fetched.
2. Blocking sizes the working set to the cache. Compute the tile size from the cache capacity; do not guess.
3. AoS is right when you touch most fields of one object; SoA when you touch one field of many. Bulk processing wants SoA.
4. Hardware prefetchers handle sequential and constant-stride access, and fail on random, pointer-chasing, and indirect patterns.
5. Good prefetching converts a latency problem into a bandwidth problem, and bandwidth is the plentiful resource.
6. Optimise in order: confirm memory-bound, classify the miss, fix layout, then loops, then prefetch.
CSCE 614 · Computer Architecture — Module 06
13