## Slide 1
UNIVERSITY OF CLAUDE
CSCE 614 — Computer Architecture
MODULE 08
Out-of-Order Execution
Running instructions early while pretending you did not.
CSCE 614 · Module 08 of 13 · original material, share freely

## Slide 2
MODULE OUTCOMES
What you will be able to do
▪ Explain register renaming and why it removes false dependences.
▪ Describe the reorder buffer and in-order retirement.
▪ Explain what limits instruction-level parallelism.
▪ Explain memory-level parallelism and why it matters more than ILP.
▪ Relate out-of-order behaviour to measured IPC.
CSCE 614 · Computer Architecture — Module 08
1
Notes: State the outcomes before the content. Every slide that follows exists to serve one of these.

## Slide 3
PART 1
The motivation
One stalled instruction should not stop everything.
CSCE 614 · Computer Architecture — Module 08
2

## Slide 4
THE PROBLEM
In-order stalls on the first miss
asm
ld r1, [r2] ; CACHE MISS -- 250 cycles
add r3, r1, r4 ; depends on r1: must wait. Correct.
mul r5, r6, r7 ; INDEPENDENT -- why should this wait?
sub r8, r9, r10 ; also independent
...
In-order: everything behind the load stalls. 250 cycles of nothing.
Out-of-order: mul and sub execute DURING the miss. By the time r1
arrives, a great deal of useful work has already been done.
The processor is not trying to be clever for its own sake. It is trying to find anything at all to do during a 250-cycle wait.
CSCE 614 · Computer Architecture — Module 08
3
Notes: Frame OoO as latency hiding, not as reordering for its own sake. That makes every mechanism that follows feel necessary.

## Slide 5
PART 2
Register renaming
Removing the dependences that were never real.
CSCE 614 · Computer Architecture — Module 08
4

## Slide 6
RENAMING
False dependences, dissolved
asm
BEFORE renaming -- r1 reused, creating a WAW/WAR tangle:
ld r1, [r2] ; writes r1 (slow)
add r3, r1, r4 ; reads r1 -- TRUE dependence (RAW)
ld r1, [r5] ; writes r1 -- FALSE (WAW) -- must it wait?
add r6, r1, r7 ; reads r1
AFTER renaming to physical registers p40, p41, ...:
ld p40, [p12]
add p41, p40, p13 ; still waits -- RAW is real
ld p42, [p14] ; INDEPENDENT -- different physical register
add p43, p42, p15 ; -> can issue immediately
Two independent load chains, discovered automatically.
Module 03 called WAR and WAW false dependences. Renaming is what makes that observation operational.
CSCE 614 · Computer Architecture — Module 08
5
Notes: The payoff: both loads can be in flight simultaneously, which is memory-level parallelism — Part 4.

## Slide 7
RENAMING
How it works
▪ The ISA exposes 16 architectural registers. The core has 150–400 physical ones.
▪ Each write to an architectural register allocates a fresh physical register.
▪ Reads are redirected to whichever physical register currently holds that architectural value.
▪ WAR and WAW vanish — they were artefacts of name reuse, and names are no longer reused.
▪ RAW remains, because it is a genuine flow of information.
▪ This is why Module 03's distinction between true and false dependences mattered.
CSCE 614 · Computer Architecture — Module 08
6

## Slide 8
PART 3
Keeping the illusion
Execute out of order; appear to execute in order.
CSCE 614 · Computer Architecture — Module 08
7

## Slide 9
ROB
The reorder buffer
▪ Instructions issue out of order, as soon as their operands are ready.
▪ Instructions retire strictly in order, from the reorder buffer.
▪ Retirement is what makes a result architecturally visible.
▪ This gives two things at once:
  – Precise exceptions — a fault appears to occur exactly where the program says.
  – Speculation recovery — mispredicted work is discarded before it ever becomes visible.
▪ ROB size (300–500 entries) bounds how far ahead the core can look.
CSCE 614 · Computer Architecture — Module 08
8
Notes: In-order retirement is the mechanism that makes the whole thing safe. Without it neither exceptions nor speculation would work.

## Slide 10
WINDOW
What limits how far ahead it can see
Resource
Typical size
Runs out when
Reorder buffer
~500 entries
A long-latency miss blocks the head
Physical registers
~200–400
Many values live at once
Load/store queue
~70–130
Many memory ops in flight
Scheduler entries
~100–200
Many waiting instructions
CSCE 614 · Computer Architecture — Module 08
9
Notes: The ROB-head point is the key one: a miss at the head blocks retirement even though execution continues behind it.

## Slide 11
PART 4
What actually limits performance
Not instruction-level parallelism — memory-level parallelism.
CSCE 614 · Computer Architecture — Module 08
10

## Slide 12
MLP matters more than ILP
KEY IDEA
Instruction-level parallelism is bounded: dependence chains in real code limit practical ILP to roughly 4–6, and wider cores show diminishing returns.
Memory-level parallelism — how many cache misses are outstanding at once — matters far more.
One miss at a time: 250 cycles each, serialised. Ten misses overlapped: still roughly 250 cycles total.
So the real value of out-of-order execution is not executing arithmetic early. It is discovering independent memory accesses and issuing them simultaneously.
CSCE 614 · Computer Architecture — Module 08
11

## Slide 13
CONSEQUENCES
What this means for your code
▪ Independent loads are enormously valuable. Multiple pointers, multiple arrays, multiple accumulators.
▪ Pointer chasing is the worst case. Each load depends on the last, so MLP is exactly 1.
  – A linked list cannot overlap any of its misses. This is the deepest reason it loses to an array.
▪ A long dependence chain through a miss is fatal — the ROB fills and the core stalls.
▪ Hyperthreading exists to supply independent work when one thread stalls.
CSCE 614 · Computer Architecture — Module 08
12
Notes: This completes the array-vs-list story begun in Module 02 and continued in 05. Three modules, one phenomenon, three levels of explanation.

## Slide 14
READING IPC
Diagnosing from counters
IPC
Means
Next step
3–4
Near peak — compute-bound
Reduce work, or vectorise
1–2
Moderate stalling
Check dependence chains, branches
0.3–1
Significant stalls
Check cache misses
< 0.3
Severely memory-bound
Layout and access pattern (Mod 06)
CSCE 614 · Computer Architecture — Module 08
13
Notes: IPC is the first number to look at, and it narrows the search immediately.

## Slide 15
What to carry forward
1. Out-of-order execution exists to find work during long memory stalls, not to reorder arithmetic for its own sake.
2. Register renaming maps 16 architectural registers onto hundreds of physical ones, dissolving the WAR and WAW dependences that were only naming artefacts.
3. Instructions issue out of order and retire in order. In-order retirement is what gives precise exceptions and safe speculation.
4. The reorder buffer bounds the lookahead window; a miss at its head blocks retirement and eventually stalls everything.
5. Memory-level parallelism matters more than instruction-level parallelism — overlapping ten misses costs about the same as one.
6. Pointer chasing has MLP of exactly 1, which is the deepest reason linked lists lose to arrays.
CSCE 614 · Computer Architecture — Module 08
14