## Slide 1
UNIVERSITY OF CLAUDE
CSCE 614 — Computer Architecture
MODULE 09
SIMD and Data-Level Parallelism
One instruction, many elements.
CSCE 614 · Module 09 of 13 · original material, share freely

## Slide 2
MODULE OUTCOMES
What you will be able to do
▪ Explain SIMD execution and its register widths.
▪ Identify loops that can and cannot vectorise.
▪ Diagnose why a compiler failed to auto-vectorise.
▪ Use intrinsics when auto-vectorisation is insufficient.
▪ Explain why SoA layout is a precondition for good vectorisation.
CSCE 614 · Computer Architecture — Module 09
1
Notes: State the outcomes before the content. Every slide that follows exists to serve one of these.

## Slide 3
PART 1
The idea
Amortise instruction overhead across many data elements.
CSCE 614 · Computer Architecture — Module 09
2

## Slide 4
SIMD
Width is throughput
c
// Scalar: one add per instruction
for (i = 0; i < N; i++) c[i] = a[i] + b[i];
// SSE (128-bit): 4 floats per instruction
// AVX2 (256-bit): 8 floats per instruction
// AVX-512 (512-bit): 16 floats per instruction
__m256 va = _mm256_load_ps(&a[i]); // 8 floats
__m256 vb = _mm256_load_ps(&b[i]);
__m256 vc = _mm256_add_ps(va, vb); // 8 additions, ONE instruction
_mm256_store_ps(&c[i], vc);
Same execution unit count, eight times the arithmetic. The instruction fetch, decode, and loop overhead are amortised across all eight elements.
CSCE 614 · Computer Architecture — Module 09
3
Notes: Worth noting that AVX-512 often downclocks the core, so 16-wide is not always 2x the 8-wide throughput.

## Slide 5
WIDTHS
The instruction set families
Extension
Width
Floats
Notes
SSE / SSE2
128-bit
4
Baseline on all x86-64
AVX / AVX2
256-bit
8
The practical default today
AVX-512
512-bit
16
Server; may reduce clock frequency
NEON (ARM)
128-bit
4
Baseline on all ARM64
SVE (ARM)
Scalable
Varies
Width-agnostic code
CSCE 614 · Computer Architecture — Module 09
4
Notes: SVE's width-agnostic model is the interesting design: the same binary adapts to whatever width the hardware has.

## Slide 6
PART 2
What blocks vectorisation
The compiler will do this for you — if you let it.
CSCE 614 · Computer Architecture — Module 09
5

## Slide 7
BLOCKERS
Why your loop did not vectorise
Blocker
Why
Fix
Pointer aliasing
Compiler cannot prove a and b are disjoint
restrict, or copy locally
Loop-carried dependence
Iteration i needs iteration i−1
Restructure, or accept it
FP reduction
Reassociation changes the result
-ffast-math, knowingly
Branches in the body
Divergent control flow
Masking, or branchless arithmetic
Non-unit stride
Gathers are slow or unavailable
Change the layout (Module 06)
Function calls
Cannot vectorise an opaque call
Inline it
CSCE 614 · Computer Architecture — Module 09
6
Notes: Aliasing is by far the most common, and `restrict` is by far the cheapest fix.

## Slide 8
ALIASING
The most common blocker
c
void add(float* c, float* a, float* b, int n) {
for (int i = 0; i < n; i++) c[i] = a[i] + b[i];
}
// Will NOT vectorise. The compiler must assume c may overlap a or b,
// in which case processing 8 at once would change the result.
void add(float* restrict c, float* restrict a,
float* restrict b, int n) {
for (int i = 0; i < n; i++) c[i] = a[i] + b[i];
}
// `restrict` promises no overlap. Vectorises immediately.
// NOTE: it is a PROMISE. Break it and you get silent corruption.
One keyword, frequently an 8× difference. C++ has no standard restrict, but every major compiler offers __restrict.
CSCE 614 · Computer Architecture — Module 09
7
Notes: Stress the 'promise' framing — restrict is unchecked and violating it is undefined behaviour.

## Slide 9
Floating-point reductions and why they resist
A REAL TRADE-OFF
Vectorising sum += a[i] requires splitting the sum into 8 partial sums and combining at the end — which reassociates the additions.
Floating-point addition is not associative: (a+b)+c ≠ a+(b+c) in general. So the vectorised result differs, usually in the last bits.
The compiler will not do this without permission, because silently changing numerical results is not its decision to make.
-ffast-math grants permission globally and enables much else besides; #pragma omp simd reduction(+:sum) grants it for one loop. Prefer the narrow version — and know that the vectorised sum is usually more accurate, since partial sums stay smaller.
CSCE 614 · Computer Architecture — Module 09
8

## Slide 10
PART 3
Layout and practice
Vectorisation is mostly a data layout problem.
CSCE 614 · Computer Architecture — Module 09
9

## Slide 11
LAYOUT
SoA is a precondition, not an optimisation
c
// AoS: x values are 32 bytes apart. A vector load needs a GATHER,
// which is slow, or 8 separate loads plus shuffles.
struct P { float x,y,z, vx,vy,vz; int id; float m; };
P p[N];
for (i...) p[i].x += p[i].vx * dt; // poor vectorisation
// SoA: x values are contiguous. One aligned 256-bit load gets 8.
struct Ps { float x[N], ..., vx[N], ...; };
for (i...) P.x[i] += P.vx[i] * dt; // vectorises perfectly
Module 06 argued for SoA on cache grounds. Vectorisation is the second, independent argument, and often the larger one.
CSCE 614 · Computer Architecture — Module 09
10
Notes: Two independent reasons converging on the same layout decision is worth pointing out explicitly.

## Slide 12
METHOD
How to approach vectorisation
▪ 1. Check whether it already vectorised. Compiler reports (-fopt-info-vec) or read the assembly.
▪ 2. If not, find out why. The compiler will usually tell you with -fopt-info-vec-missed.
▪ 3. Remove the blocker. restrict, inlining, layout change, pragma.
▪ 4. Only then consider intrinsics. They are unportable, verbose, and hard to maintain.
▪ 5. Measure. If the loop is memory-bound, vectorising the arithmetic changes nothing.
Point 5 is the one people skip. 8× the arithmetic on a bandwidth-limited loop is 0× the speedup.
CSCE 614 · Computer Architecture — Module 09
11

## Slide 13
Vectorising a memory-bound loop does nothing
THE COMMON DISAPPOINTMENT
SIMD multiplies arithmetic throughput. If the loop is waiting on memory, there was never an arithmetic shortage.
Check first: compute the arithmetic intensity — operations per byte loaded. Below roughly 1 flop/byte you are almost certainly bandwidth-bound and SIMD will not help.
This is why Module 06 comes before Module 09. Fix the memory behaviour, then vectorise what remains.
The exception: SIMD loads also move more bytes per instruction, so there is sometimes a modest benefit even when bandwidth-bound. Modest, not 8×.
CSCE 614 · Computer Architecture — Module 09
12

## Slide 14
PERSPECTIVE
SIMD and the courses around it
Where
Connection
CSCE 641
Shaders are SIMD. A GPU warp is 32-wide SIMD with a nicer programming model
CSCE 735
SIMD is the finest-grained level of the parallelism hierarchy
Module 10
GPUs take this idea much further — next module
Module 06
SoA layout is required for both cache and vector efficiency
CSCE 614 · Computer Architecture — Module 09
13

## Slide 15
What to carry forward
1. SIMD amortises instruction overhead across 4, 8, or 16 elements. AVX2 at 256 bits is the practical default.
2. Pointer aliasing is the most common vectorisation blocker, and restrict is an unchecked promise that fixes it.
3. Floating-point reductions resist vectorisation because reassociation changes results. Grant permission per loop, not globally.
4. Struct-of-arrays is a precondition for good vectorisation, not merely a cache optimisation — two independent arguments, same conclusion.
5. Let the compiler vectorise; reach for intrinsics only after removing blockers and measuring.
6. Vectorising a memory-bound loop achieves nothing. Check arithmetic intensity first.
CSCE 614 · Computer Architecture — Module 09
14