## Slide 1
UNIVERSITY OF CLAUDE
CSCE 614 — Computer Architecture
MODULE 10
GPUs as Throughput Machines
A different answer to the same memory problem.
CSCE 614 · Module 10 of 13 · original material, share freely

## Slide 2
MODULE OUTCOMES
What you will be able to do
▪ Contrast latency-oriented and throughput-oriented design.
▪ Explain SIMT execution and warp divergence.
▪ Explain memory coalescing and its importance.
▪ Explain occupancy and what limits it.
▪ Decide whether a workload suits a GPU.
CSCE 614 · Computer Architecture — Module 10
1
Notes: State the outcomes before the content. Every slide that follows exists to serve one of these.

## Slide 3
PART 1
Two philosophies
The same memory wall, answered in opposite ways.
CSCE 614 · Computer Architecture — Module 10
2

## Slide 4
DESIGN
Hide latency, or tolerate it
CPU — latency oriented
▪ Make one thread fast.
▪ Large caches, deep out-of-order windows, branch prediction, speculation.
▪ Most of the die is control logic and cache.
  – Few cores, each enormous.
  – Good at: everything, including irregular work.
GPU — throughput oriented
▪ Make many threads collectively fast.
▪ Small caches, in-order, no speculation.
▪ Most of the die is arithmetic units.
  – Thousands of threads resident at once.
  – Good at: regular, data-parallel work with high arithmetic intensity.
CSCE 614 · Computer Architecture — Module 10
3
Notes: Same problem, opposite answers. The CPU avoids the wait; the GPU finds other work during it.

## Slide 5
How a GPU hides memory latency
KEY IDEA
A CPU hides a cache miss with out-of-order execution: find independent instructions within one thread. The window is a few hundred instructions.
A GPU hides it by switching threads. When a warp stalls on memory, another resident warp issues in the very next cycle. With 64 warps resident, there is almost always something ready.
Context switching is free because every thread's registers stay resident — that is what the enormous register file is for.
The consequence: a GPU needs many more threads than cores to perform well. Under-occupancy is the most common reason GPU code disappoints.
CSCE 614 · Computer Architecture — Module 10
4

## Slide 6
PART 2
SIMT execution
SIMD with a thread-shaped programming model.
CSCE 614 · Computer Architecture — Module 10
5

## Slide 7
SIMT
Warps: 32 threads in lockstep
▪ Threads are grouped into warps of 32 (NVIDIA) or waves of 32/64 (AMD).
▪ All threads in a warp execute the same instruction each cycle.
▪ You write scalar per-thread code; the hardware executes it 32 lanes wide.
  – This is SIMD with a far more pleasant programming model.
▪ Divergence: if threads in a warp take different branches, both paths execute with inactive lanes masked off.
  – Worst case — all 32 take different paths — costs 32×.
CSCE 614 · Computer Architecture — Module 10
6
Notes: This is exactly Module 07 of CSCE 641. Same mechanism, explained from the hardware side.

## Slide 8
DIVERGENCE
What divergence costs
c
// BAD: threads within a warp diverge every time
if (threadIdx.x % 2 == 0) heavy_a();
else heavy_b();
// Both branches execute for the whole warp. Cost = a + b.
// GOOD: divergence occurs at warp granularity
if ((threadIdx.x / 32) % 2 == 0) heavy_a();
else heavy_b();
// Each warp takes one path. Cost = max(a, b) per warp.
// BEST: no divergence at all
result = select(cond, value_a, value_b);
Divergence costs nothing if it happens at warp boundaries. Restructuring so that neighbouring threads agree is often the single largest GPU optimisation.
CSCE 614 · Computer Architecture — Module 10
7
Notes: The 'divergence at warp granularity is free' point is the actionable one, and it is often missed.

## Slide 9
PART 3
Memory
Coalescing is the single most important GPU optimisation.
CSCE 614 · Computer Architecture — Module 10
8

## Slide 10
COALESCING
Neighbouring threads must touch neighbouring addresses
c
// COALESCED: thread i reads element i.
// 32 consecutive floats = 128 bytes = ONE memory transaction.
float v = data[blockIdx.x * blockDim.x + threadIdx.x];
// UNCOALESCED: thread i reads element i*32.
// 32 separate transactions, each using 4 of 128 bytes fetched.
float v = data[(blockIdx.x * blockDim.x + threadIdx.x) * 32];
// -> 32x the memory traffic for the same data
// This is Module 06's stride problem, with a 32x penalty
// instead of a 16x one.
The GPU fetches memory in wide transactions. If a warp's 32 threads touch 32 scattered addresses, you pay 32 transactions and use a fraction of each.
CSCE 614 · Computer Architecture — Module 10
9
Notes: Coalescing is to GPUs what cache line utilisation is to CPUs — same principle, harsher penalty.

## Slide 11
MEMORY SPACES
The GPU memory hierarchy
Space
Scope
Latency
Use for
Registers
One thread
~0
Everything you can
Shared / LDS
Thread block
~20 cyc
Explicit tiling
L1 / texture
SM
~30 cyc
Automatic caching
L2
Device
~200 cyc
Automatic
Global (VRAM)
Device
~400–600 cyc
Bulk data
CSCE 614 · Computer Architecture — Module 10
10
Notes: Shared memory is the interesting one: a programmer-managed cache, which is how blocking (Module 06) is done explicitly on a GPU.

## Slide 12
OCCUPANCY
Keeping enough warps resident
▪ Occupancy = resident warps / maximum possible.
▪ Limited by whichever runs out first:
  – Registers — a register-hungry kernel allows fewer threads.
  – Shared memory — a block using a lot allows fewer blocks.
  – Block size — too small wastes scheduling slots.
▪ Higher occupancy means more warps available to hide latency.
▪ But higher is not always better — a kernel with high arithmetic intensity may do better with more registers and fewer warps.
Occupancy is a means to latency hiding, not a goal in itself.
CSCE 614 · Computer Architecture — Module 10
11

## Slide 13
JUDGEMENT
Does this workload suit a GPU?
Suits a GPU
Suits a CPU
Thousands of independent work items
Few threads, or heavy inter-dependence
Regular, predictable memory access
Pointer chasing, irregular structures
High arithmetic intensity
Low intensity — PCIe transfer dominates
Little divergence
Heavily data-dependent control flow
Data already on the device
Data must round-trip over PCIe
CSCE 614 · Computer Architecture — Module 10
12
Notes: The transfer cost is the one that kills otherwise-suitable workloads. Always count it.

## Slide 14
Count the transfer
THE USUAL MISTAKE
PCIe gives roughly 16–32 GB/s. GPU memory gives 500–1000 GB/s.
So moving data to the device and back can cost far more than the computation saves. A kernel that is 50× faster is worthless if the transfer takes 100× the kernel time.
Rule: the arithmetic per byte transferred must be high, or the data must already live on the device and stay there.
This is why graphics works so well: the vertex and texture data lives in VRAM permanently and is used every frame. It is also why many 'GPU-accelerated' library calls disappoint.
CSCE 614 · Computer Architecture — Module 10
13

## Slide 15
What to carry forward
1. CPUs hide latency within one thread; GPUs tolerate it by switching among thousands. Same memory wall, opposite answers.
2. Context switching is free on a GPU because every resident thread's registers stay in place — hence the enormous register file.
3. SIMT is SIMD with a per-thread programming model. Warp divergence executes both paths, costing up to 32×.
4. Divergence at warp granularity is free. Restructuring so neighbouring threads agree is often the biggest win.
5. Coalescing is Module 06's stride problem with a 32× penalty: neighbouring threads must touch neighbouring addresses.
6. Count the PCIe transfer. A 50× kernel is worthless if moving the data costs more than the computation saves.
CSCE 614 · Computer Architecture — Module 10
14