## Slide 1
UNIVERSITY OF CLAUDE
CSCE 614 — Computer Architecture
MODULE 11
Multicore and Cache Coherence
Many caches, one memory, and the protocol that reconciles them.
CSCE 614 · Module 11 of 13 · original material, share freely

## Slide 2
MODULE OUTCOMES
What you will be able to do
▪ Explain why coherence is needed and what it guarantees.
▪ Describe the MESI protocol states and transitions.
▪ Explain false sharing and detect it.
▪ Explain why atomic operations cost what they do.
▪ Explain NUMA and its implications for data placement.
CSCE 614 · Computer Architecture — Module 11
1
Notes: State the outcomes before the content. Every slide that follows exists to serve one of these.

## Slide 3
PART 1
The problem
Private caches plus shared memory equals disagreement.
CSCE 614 · Computer Architecture — Module 11
2

## Slide 4
THE PROBLEM
Two cores, two answers
text
Initially x = 0 in memory.
Core 0 Core 1
load x -> cache has 0 load x -> cache has 0
x = 1 -> cache has 1
load x -> still reads 0 from ITS cache
Core 1 is reading stale data. Without a protocol, nothing
prevents this -- each core's cache is private and neither
knows the other exists.
COHERENCE: a read must return the most recent write.
Coherence is about a single location seen consistently. Consistency — the ordering of operations across several locations — is a separate and harder problem (Module 12).
CSCE 614 · Computer Architecture — Module 11
3
Notes: Students conflate coherence and consistency constantly. Distinguish them early and repeat it.

## Slide 5
PART 2
MESI
Four states per cache line, and a protocol to move between them.
CSCE 614 · Computer Architecture — Module 11
4

## Slide 6
MESI
The four states
State
Means
Other caches
Memory
Modified
I have it and have changed it
None have it
Stale
Exclusive
I have it, unchanged, alone
None have it
Current
Shared
I have it, read-only
Others may have it
Current
Invalid
I do not have it
—
—
CSCE 614 · Computer Architecture — Module 11
5
Notes: The E state is the useful optimisation: a write to an E line needs no bus traffic at all.

## Slide 7
MESI
How it behaves
▪ Read miss: fetch the line. If nobody else has it → E; if others do → S for everyone.
▪ Write to S: broadcast an invalidate; all other copies → I; mine → M.
▪ Write to E: silently → M. No traffic at all.
  – This is why E exists — private data is written without any bus transaction.
▪ Another core reads my M line: I supply it and drop to S.
▪ Enforced by snooping on a bus, or by a directory at scale.
CSCE 614 · Computer Architecture — Module 11
6

## Slide 8
PART 3
False sharing
The most common and most invisible parallel performance bug.
CSCE 614 · Computer Architecture — Module 11
7

## Slide 9
Coherence operates on lines, not variables
THE BUG
Two threads write to two different variables that happen to occupy the same 64-byte cache line.
Logically there is no sharing. The hardware cannot tell: it tracks lines, not variables. Every write invalidates the other core's copy.
The line ping-pongs between cores on every write. Each access becomes a coherence miss costing hundreds of cycles.
A parallel program can be slower than the serial version with perfect logical independence. Nothing in the source suggests a problem.
CSCE 614 · Computer Architecture — Module 11
8

## Slide 10
FALSE SHARING
The bug and the fix
c
// BAD: counters[0..7] share one or two cache lines
long counters[8];
// thread i: counters[i]++; <- ping-pongs constantly
// GOOD: pad each to its own line
struct alignas(64) Counter { long v; char pad[56]; };
Counter counters[8];
// thread i: counters[i].v++; <- no sharing at all
// BETTER: accumulate locally, combine at the end
long local = 0;
for (...) local++; // in a register
counters[tid].v = local; // ONE write at the end
The third version is usually best: it avoids both false sharing and the coherence traffic of frequent writes to shared lines.
CSCE 614 · Computer Architecture — Module 11
9
Notes: The local-accumulation pattern generalises: minimise writes to any line another core touches.

## Slide 11
PART 4
Atomics and NUMA
What synchronisation costs, and where memory actually lives.
CSCE 614 · Computer Architecture — Module 11
10

## Slide 12
ATOMICS
Why atomic operations are expensive
▪ An atomic read-modify-write must obtain the line in M state exclusively.
▪ Under contention, that line moves between cores constantly.
  – Uncontended atomic: ~20 cycles.
  – Contended atomic: 100–500+ cycles, and worse with more cores.
▪ Atomics do not scale. A single contended counter is a bottleneck at any core count.
▪ Fix: per-thread counters combined at the end — the same pattern as the false-sharing fix.
CSCE 614 · Computer Architecture — Module 11
11
Notes: The scaling point matters: adding cores to a contended-atomic workload makes it slower, not faster.

## Slide 13
NUMA
Not all memory is equally far
Access
Latency
Bandwidth
Local socket memory
~90 ns
Full
Remote socket memory
~140 ns
Reduced — crosses the interconnect
CSCE 614 · Computer Architecture — Module 11
12
Notes: First-touch is the practical consequence and the usual bug: serial initialisation puts everything on one node.

## Slide 14
PRACTICE
Writing scalable parallel code
▪ Minimise sharing. Per-thread data combined at the end beats shared data protected by locks.
▪ Pad shared structures to 64-byte boundaries.
▪ Avoid contended atomics. Accumulate locally; combine once.
▪ Initialise in parallel so NUMA first-touch distributes pages.
▪ Pin threads when it matters, so the OS does not migrate them away from their data.
▪ Diagnose with cache-coherence counters, not with guesswork.
A parallel speedup well below the core count almost always means sharing, not insufficient parallelism.
CSCE 614 · Computer Architecture — Module 11
13

## Slide 15
What to carry forward
1. Coherence guarantees a read returns the most recent write to one location. Consistency — ordering across locations — is Module 12.
2. MESI tracks four states per line. The Exclusive state exists so writes to private data generate no bus traffic.
3. False sharing: two threads writing different variables in the same 64-byte line. Logically independent, physically contended, invisible in source.
4. A contended atomic costs 100–500+ cycles and gets worse with more cores. Atomics do not scale.
5. The fix for both is the same: accumulate per-thread, combine once.
6. NUMA pages land near the core that first touches them, so parallel initialisation matters as much as parallel computation.
CSCE 614 · Computer Architecture — Module 11
14