## Slide 1
UNIVERSITY OF CLAUDE
CSCE 614 — Computer Architecture
MODULE 12
Memory Consistency and Synchronization
Why your multithreaded code does not do what it says.
CSCE 614 · Module 12 of 13 · original material, share freely

## Slide 2
MODULE OUTCOMES
What you will be able to do
▪ Explain sequential consistency and why no hardware implements it.
▪ Explain store buffering and the reorderings real hardware permits.
▪ Use memory barriers and acquire/release semantics correctly.
▪ Explain why the compiler reorders too.
▪ Explain why lock-free programming is difficult.
CSCE 614 · Computer Architecture — Module 12
1
Notes: State the outcomes before the content. Every slide that follows exists to serve one of these.

## Slide 3
PART 1
The surprise
A program that cannot produce an outcome, producing it.
CSCE 614 · Computer Architecture — Module 12
2

## Slide 4
DEKKER
The result that should be impossible
c
// Initially: x = 0, y = 0
// Thread 1 // Thread 2
x = 1; y = 1;
r1 = y; r2 = x;
// Reason about all interleavings of a sequential execution:
// both stores happen before at least one of the loads,
// so at least one load must see 1.
// r1 == 0 && r2 == 0 is IMPOSSIBLE.
// On real x86 hardware, r1 == 0 && r2 == 0 HAPPENS.
Not a compiler bug and not a race in the usual sense. The hardware is behaving as specified — the specification is just not what you assumed.
CSCE 614 · Computer Architecture — Module 12
3
Notes: Run this. Seeing it happen on real hardware is the only thing that makes the module stick.

## Slide 5
Store buffers
THE EXPLANATION
A store must obtain the cache line in Modified state, which can take hundreds of cycles. Stalling the core on every store would be ruinous.
So stores go into a store buffer and the core proceeds immediately. The store becomes visible to other cores later.
Meanwhile loads may read ahead, from cache or from the local store buffer.
So Thread 1's store to x may still be sitting in its store buffer when Thread 2 loads x. Both threads see the old value. The hardware is correct; sequential reasoning was wrong.
CSCE 614 · Computer Architecture — Module 12
4

## Slide 6
PART 2
Consistency models
A contract about what reorderings are permitted.
CSCE 614 · Computer Architecture — Module 12
5

## Slide 7
MODELS
What each model allows
Model
Reorders
Found on
Sequential (SC)
Nothing
No real hardware
TSO
Store→Load only
x86-64
Weak / relaxed
Almost anything
ARM, POWER, RISC-V
CSCE 614 · Computer Architecture — Module 12
6
Notes: x86's TSO is relatively strong, which is why code that works on x86 often breaks on ARM. Test on both.

## Slide 8
Why weak code works on x86 and breaks on ARM
A REAL PORTABILITY TRAP
x86 provides TSO: only store→load reordering is permitted. A great deal of incorrectly synchronised code happens to work.
ARM and POWER permit store→store, load→load, and load→store reordering as well. The same code breaks.
This is why a concurrency bug can lie dormant for years and then appear when a product ships on ARM.
Do not infer correctness from testing. Reason from the memory model, use the language's atomics, and test on weakly ordered hardware as well.
CSCE 614 · Computer Architecture — Module 12
7

## Slide 9
PART 3
Barriers and ordering
Telling the hardware and the compiler what you require.
CSCE 614 · Computer Architecture — Module 12
8

## Slide 10
ORDERING
Acquire and release
Operation
Guarantees
Use for
acquire (load)
Nothing after it moves before it
Taking a lock; reading a flag
release (store)
Nothing before it moves after it
Releasing a lock; setting a flag
acq_rel
Both
Read-modify-write
seq_cst
A single global order of all seq_cst ops
The safe default
relaxed
Atomicity only, no ordering
Counters you only read at the end
CSCE 614 · Computer Architecture — Module 12
9
Notes: Acquire/release is the right mental model: release publishes everything written before it; acquire sees everything published.

## Slide 11
PATTERN
The publish/subscribe idiom
c
// PRODUCER // CONSUMER
data = compute(); while (!ready.load(acquire))
ready.store(true, release); spin;
use(data); // guaranteed to see
// the compute() result
// The release store publishes everything written BEFORE it.
// The acquire load sees everything that was published.
// Together they create a happens-before edge across threads.
// With relaxed ordering, the consumer may see ready == true
// while `data` still holds its old value.
This pairing is the foundation of almost all lock-free code. Release publishes; acquire subscribes.
CSCE 614 · Computer Architecture — Module 12
10
Notes: If students remember one thing from this module, it should be this pattern.

## Slide 12
COMPILERS TOO
The compiler reorders as well
▪ Hardware reordering is only half the problem. Compilers reorder, cache values in registers, and delete 'redundant' loads.
▪ A spin loop on a non-atomic variable can be hoisted into an infinite loop.
  – The compiler proves nothing in the loop modifies it — which is true single-threaded.
▪ volatile is not a synchronisation primitive in C or C++.
  – It prevents some compiler optimisations. It provides no hardware ordering and no atomicity.
▪ Use std::atomic (or C11 _Atomic). It constrains both compiler and hardware.
CSCE 614 · Computer Architecture — Module 12
11
Notes: The volatile misconception is extremely common and worth attacking directly.

## Slide 13
PART 4
Practice
What to actually do.
CSCE 614 · Computer Architecture — Module 12
12

## Slide 14
COSTS
Synchronisation, priced
Mechanism
Uncontended
Contended
Relaxed atomic load
~1 cycle
~1 cycle
Acquire/release
~1–20 cycles
Coherence traffic
seq_cst store (x86)
~20–40 cycles
Worse
Uncontended mutex
~20 cycles
—
Contended mutex
—
~1,000+ (syscall, context switch)
CSCE 614 · Computer Architecture — Module 12
13
Notes: An uncontended mutex is cheap. The cost is entirely in contention, which is an argument for reducing sharing rather than for avoiding locks.

## Slide 15
ADVICE
How to write correct concurrent code
▪ Use a mutex unless you have measured that it is the problem. Uncontended locks are cheap and obviously correct.
▪ Prefer immutability and message passing over shared mutable state.
▪ If you must go lock-free: use std::atomic with explicit ordering, document the reasoning, and test under a race detector and on ARM.
▪ Never invent a synchronisation primitive without a proof. This is one area where cleverness is reliably punished.
▪ Use tools: ThreadSanitizer, helgrind, stress tests on weak hardware.
Lock-free code that is subtly wrong usually passes every test you write for it.
CSCE 614 · Computer Architecture — Module 12
14

## Slide 16
What to carry forward
1. Dekker's example produces an outcome that sequential reasoning says is impossible, because store buffers delay visibility.
2. No real hardware implements sequential consistency. x86 gives TSO; ARM and POWER are much weaker.
3. Code that is incorrectly synchronised often works on x86 and fails on ARM. Do not infer correctness from testing.
4. Release publishes everything written before it; acquire sees everything published. That pairing underlies almost all lock-free code.
5. The compiler reorders too, and volatile is not a synchronisation primitive. Use std::atomic.
6. Uncontended mutexes are cheap. Reach for lock-free only after measuring, and never invent a primitive without a proof.
CSCE 614 · Computer Architecture — Module 12
15