## Slide 1
UNIVERSITY OF CLAUDE
CSCE 614 — Computer Architecture
MODULE 13
Energy, Scaling, and Specialization
Why the free lunch ended, and what replaced it.
CSCE 614 · Module 13 of 13 · original material, share freely

## Slide 2
MODULE OUTCOMES
What you will be able to do
▪ Explain Dennard scaling and why its end changed everything.
▪ Explain dark silicon and the shift to multicore.
▪ Explain why specialised hardware is more efficient.
▪ Describe the current landscape of accelerators.
▪ Build a working cost model of a modern machine.
CSCE 614 · Computer Architecture — Module 13
1
Notes: State the outcomes before the content. Every slide that follows exists to serve one of these.

## Slide 3
PART 1
The free lunch
Thirty years of programs getting faster without being changed.
CSCE 614 · Computer Architecture — Module 13
2

## Slide 4
DENNARD SCALING
Why it worked
P = C · V² · f
Dynamic power: capacitance, voltage squared, frequency.
shrink by k: C ↓ k, V ↓ k, f ↑ k
Dennard's observation: smaller transistors run at lower voltage.
power density stays constant
More transistors, faster, same power. For thirty years.
Moore's law gave more transistors; Dennard scaling let you use them for free. The second one is what actually ended.
CSCE 614 · Computer Architecture — Module 13
3
Notes: Students conflate Moore's law ending with Dennard scaling ending. The distinction is the whole module.

## Slide 5
Dennard scaling ended around 2005
THE TURNING POINT
Voltage stopped scaling, because leakage current rises sharply as threshold voltage falls — a transistor that does not switch off cleanly wastes power continuously.
With V fixed, shrinking transistors raises power density. Clock frequency became limited by heat rather than by switching speed.
Clock speeds flattened at 3–4 GHz, where they remain twenty years later.
Moore's law continued for some time — transistors kept getting smaller. What ended was the ability to use them all at full speed. That is dark silicon: a chip with more transistors than it can power simultaneously.
CSCE 614 · Computer Architecture — Module 13
4

## Slide 6
PART 2
The responses
Three strategies, in historical order.
CSCE 614 · Computer Architecture — Module 13
5

## Slide 7
RESPONSES
How the industry adapted
Response
Idea
Cost to you
Multicore
Many simpler cores instead of one fast one
You must parallelise. Amdahl applies
Heterogeneity
Big cores + little cores on one die
Scheduling complexity; variable performance
Specialisation
Fixed-function units for specific work
Only helps if your work matches
CSCE 614 · Computer Architecture — Module 13
6
Notes: Multicore was the first and bluntest response, and it transferred the burden to software. That transfer is why CSCE 735 exists.

## Slide 8
The burden moved to software
THE CONSEQUENCE
Before 2005, a program got faster every year by doing nothing. Clock speeds rose and single-thread performance rose with them.
After 2005, performance came from more cores, which benefit only programs written to use them.
Single-thread performance has improved maybe 2–3× in twenty years, from microarchitecture rather than frequency.
This is why parallel programming stopped being specialised and became general. It is also why Amdahl's law from Module 01 is a practical constraint rather than a theoretical curiosity.
CSCE 614 · Computer Architecture — Module 13
7

## Slide 9
PART 3
Specialisation
Why fixed-function hardware wins by orders of magnitude.
CSCE 614 · Computer Architecture — Module 13
8

## Slide 10
WHY
Where a general-purpose core spends its energy
▪ A 32-bit integer add costs well under 1 pJ.
▪ Fetching, decoding, renaming, scheduling, and retiring the instruction that performs it costs far more.
▪ In a general-purpose core, the arithmetic is a small fraction of the energy.
▪ Fixed-function hardware removes the overhead entirely: no fetch, no decode, no scheduling, data flowing through dedicated logic.
▪ The result is routinely 10–1000× better energy efficiency for the task it was built for.
CSCE 614 · Computer Architecture — Module 13
9
Notes: The energy breakdown is the explanation people usually lack. Instruction overhead dominating arithmetic is the key fact.

## Slide 11
ACCELERATORS
The current landscape
Accelerator
For
Why it wins
GPU
Data-parallel throughput
Area spent on ALUs, not control
Video codec block
H.264/H.265/AV1
Fixed function; ~100× efficiency
Tensor/matrix units
Matrix multiply
Systolic dataflow; minimal data movement
Ray tracing units
BVH traversal, intersection
Fixed-function traversal
DSP / NPU
Signal processing, inference
Specialised datapaths, low precision
CSCE 614 · Computer Architecture — Module 13
10
Notes: The RT cores row connects directly to CSCE 647: hardware acceleration changed what is feasible in real-time rendering.

## Slide 12
Specialisation has a cost too
THE TRADE
Fixed-function hardware does one thing. If the algorithm changes, the silicon is wasted — and silicon takes years to design and fabricate.
A video block that decodes H.265 is useless for AV1. Tensor units tuned for one numeric format are poor for another.
So specialisation is a bet that the workload is stable. It has paid off for video, graphics, and dense linear algebra, all of which have been stable for a decade or more.
It is a worse bet for anything still changing rapidly — which is why programmable GPUs beat fixed-function graphics pipelines in the first place.
CSCE 614 · Computer Architecture — Module 13
11

## Slide 13
PART 4
A cost model
What this course was for.
CSCE 614 · Computer Architecture — Module 13
12

## Slide 14
SYNTHESIS
The questions to ask about any slow code
Question
Check
Module
Am I compute- or memory-bound?
IPC
01, 08
Am I missing in cache?
Miss rates by level
05, 06
Am I missing in the TLB?
dTLB misses
07
Am I mispredicting branches?
branch-miss rate
04
Am I vectorised?
Assembly, vec reports
09
Am I sharing between cores?
perf c2c
11
Would this suit a GPU?
Arithmetic intensity
10
CSCE 614 · Computer Architecture — Module 13
13
Notes: This table is the course's deliverable. Students should be able to work down it without prompting.

## Slide 15
THE MODEL
What you should now believe
▪ Memory dominates. A 2% miss rate costs more than a 5% branch misprediction rate by a factor of ten.
▪ Latency is hidden, not removed. Caches, prefetching, out-of-order, and multithreading are all latency hiding.
▪ Parallelism is everywhere — lanes, pipelines, cores, devices — and each level has a different cost.
▪ Layout decides performance more often than algorithms do, once the algorithm is reasonable.
▪ Measure. Every claim in this course is checkable on your own machine in an afternoon.
CSCE 614 · Computer Architecture — Module 13
14

## Slide 16
END
Where this course leaves you
▪ You can predict, roughly, what will make a loop slow — before running it.
▪ You can diagnose a slow program from counters rather than guesswork.
▪ You know why CSCE 629's model is wrong, and by how much.
▪ CSCE 641 is where cache behaviour becomes frame time.
▪ CSCE 735 takes the parallelism hierarchy seriously.
▪ CSCE 611 explains the operating system on top of this hardware.
CSCE 614 · Computer Architecture — Module 13
15

## Slide 17
What to carry forward
1. Dennard scaling — not Moore's law — is what ended around 2005, when voltage stopped scaling because of leakage.
2. Dark silicon: a chip can contain more transistors than it can power at once. Clock speeds have been flat at 3–4 GHz for twenty years.
3. The response was multicore, which transferred the performance burden to software and made Amdahl's law a practical constraint.
4. In a general-purpose core, instruction overhead dominates the arithmetic energy. Fixed-function hardware removes it, winning 10–1000×.
5. Specialisation bets that the workload is stable. It has paid for video, graphics, and dense linear algebra.
6. The deliverable of this course is a diagnostic checklist: IPC, cache misses, TLB, branches, vectorisation, sharing.
CSCE 614 · Computer Architecture — Module 13
16