## Slide 1
UNIVERSITY OF CLAUDE
CSCE 620 — Computational Geometry
MODULE 11
Visibility and Motion Planning
What can be seen, and how to get there.
CSCE 620 · Module 11 of 13 · original material, share freely

## Slide 2
MODULE OUTCOMES
What you will be able to do
▪ Compute a visibility polygon by angular sweep.
▪ Build a visibility graph and use it for shortest paths.
▪ Explain configuration space and the Minkowski sum.
▪ Explain how a navigation mesh is built and why.
▪ Compare roadmap, sampling, and grid-based planners.
CSCE 620 · Computational Geometry — Module 11
1
Notes: State the outcomes before the content. Every slide that follows exists to serve one of these.

## Slide 3
PART 1
Visibility polygons
An angular sweep.
CSCE 620 · Computational Geometry — Module 11
2

## Slide 4
Visibility from a point is a rotational sweep
THE ALGORITHM
Sort all obstacle vertices by angle about the viewpoint. Sweep a ray through them in order.
Maintain the obstacle edges the ray currently crosses, ordered by distance — the status structure (Module 04), now angular.
The nearest edge is what is visible in that direction. When the nearest edge changes, emit a vertex of the visibility polygon.
O(n log n), dominated by the angular sort. This is the basis of 2D field-of-view, line-of-sight, and 2D dynamic lighting.
CSCE 620 · Computational Geometry — Module 11
3

## Slide 5
The degeneracies are the usual suspects
WHAT BREAKS IT
Collinear vertices — two obstacle corners at the same angle from the viewpoint. The sweep order between them is undefined.
The viewpoint exactly on an edge or at a vertex, which is extremely common when the viewer is an agent standing against a wall.
Angle comparison invites atan2, which destroys exactness — compare with orient instead (Module 03 §1).
And the sweep wraps around at ±π, so the comparator must be a cyclic one, which is a classic source of subtle bugs.
CSCE 620 · Computational Geometry — Module 11
4

## Slide 6
PART 2
Configuration space
The idea that makes planning tractable.
CSCE 620 · Computational Geometry — Module 11
5

## Slide 7
Shrink the robot to a point, grow the obstacles
THE CENTRAL IDEA OF MOTION PLANNING
Planning for a shape is hard; planning for a point is easy.
So transform the problem: replace each obstacle O with the Minkowski sum O ⊕ (−R), where R is the robot. The robot becomes a single point.
A point path through the grown obstacles corresponds exactly to a collision-free motion of the original shape.
For a translating convex robot the sum is convex and computable in O(n + m) by merging edges in angular order — which is cheap. Rotation adds a dimension and makes it much harder.
CSCE 620 · Computational Geometry — Module 11
6

## Slide 8
MINKOWSKI
The sum, and its one easy case
A ⊕ B = { a + b : a ∈ A, b ∈ B }
Every point of A translated by every point of B.
Convex ⊕ convex: merge the edge vectors by angle
O(n + m), and the result is convex with n + m edges.
Non-convex: O(n²m²) in the worst case
Which is why decomposition into convex pieces (Module 03) comes first.
The convex case being linear is why convex decomposition is everywhere in collision and planning.
CSCE 620 · Computational Geometry — Module 11
7
Notes: This is the same reason GJK needs convexity (Module 12).

## Slide 9
PART 3
Roadmaps
Precompute the connectivity.
CSCE 620 · Computational Geometry — Module 11
8

## Slide 10
PLANNERS
Four ways to plan a path
Method
Idea
Character
Visibility graph
Connect mutually visible vertices; shortest path
Optimal path. O(n²) graph
Navigation mesh
Convex cells covering walkable space
What games use. Funnel for the path
Grid / A*
Discretise; search
Simple; paths look discretised
PRM
Sample configurations; connect
High dimensions; multi-query
RRT / RRT*
Grow a tree toward random samples
Single-query; RRT* is optimal in the limit
CSCE 620 · Computational Geometry — Module 11
9
Notes: The optimal-vs-natural distinction is the key design point.

## Slide 11
Why a navmesh beats a grid
THE ENGINE'S ACTUAL CHOICE
A grid discretises space uniformly, so a large open room costs as many cells as a cluttered corridor, and paths are constrained to grid directions.
A navmesh covers the walkable surface with convex polygons, so one polygon can be an entire room and the cell count tracks the complexity of the geometry.
Convexity is the point: within one cell, straight-line movement is guaranteed collision-free, so the path only needs cell-to-cell decisions.
Then the funnel algorithm pulls the path taut through the sequence of shared edges, producing the shortest path within that corridor — which looks natural rather than stepped.
CSCE 620 · Computational Geometry — Module 11
10

## Slide 12
BUILDING ONE
How a navmesh is generated
▪ 1. Voxelise the world geometry and mark cells as solid or open.
▪ 2. Filter by walkability — slope limit, step height, agent crouch height, ledge detection.
▪ 3. Extract the walkable surface and build a distance field over it.
▪ 4. Watershed-partition into regions, then trace region contours.
▪ 5. Simplify the contours and triangulate (Module 05), then merge into convex polygons.
▪ And erode by the agent radius — which is the Minkowski sum of Part 2, applied.
Recast does exactly this, and it is the standard open implementation.
CSCE 620 · Computational Geometry — Module 11
11

## Slide 13
PART 4
Sampling
When the configuration space is too big to build.
CSCE 620 · Computational Geometry — Module 11
12

## Slide 14
Sampling-based planning gives up completeness
THE TRADE
A robot arm with seven joints has a seven-dimensional configuration space. Building it explicitly is hopeless.
So sample it: pick random configurations, keep the collision-free ones, connect nearby pairs, and search the resulting graph.
This is probabilistically complete — it finds a path if one exists, given enough samples. It cannot report that none exists.
And it struggles with narrow passages, which have small volume and so are rarely sampled. That is the characteristic failure mode, and most of the literature is about mitigating it.
CSCE 620 · Computational Geometry — Module 11
13

## Slide 15
What to carry forward
1. A visibility polygon is an angular sweep maintaining edges ordered by distance; the nearest edge is what is visible.
2. Configuration space shrinks the robot to a point and grows obstacles by the Minkowski sum, turning a shape-planning problem into a point-planning one.
3. Minkowski sum of two convex polygons is O(n + m) by merging edge vectors in angular order — which is why convex decomposition comes first.
4. Visibility graphs give optimal paths; navmeshes give fast natural-looking ones, which is what games choose.
5. A navmesh's convex cells guarantee straight-line movement within a cell, and the funnel algorithm pulls the corridor path taut.
6. Sampling-based planners are only probabilistically complete and fail characteristically on narrow passages.
CSCE 620 · Computational Geometry — Module 11
14