## Slide 1
UNIVERSITY OF CLAUDE
CSCE 645 — Geometric Modeling
MODULE 05
Surfaces: Tensor Products and Patches
Curves in two directions, and where the construction runs out.
CSCE 645 · Module 05 of 13 · original material, share freely

## Slide 2
MODULE OUTCOMES
What you will be able to do
▪ Construct tensor-product Bézier and B-spline surfaces.
▪ Evaluate a patch and compute its normals and derivatives.
▪ Explain why tensor products force quadrilateral topology.
▪ Explain trimming and why it is necessary and awkward.
▪ Explain cross-patch continuity and why it is hard.
CSCE 645 · Geometric Modeling — Module 05
1
Notes: State the outcomes before the content. Every slide that follows exists to serve one of these.

## Slide 3
PART 1
The construction
Take a curve scheme and apply it twice.
CSCE 645 · Geometric Modeling — Module 05
2

## Slide 4
TENSOR PRODUCT
Curves in two parameters
S(u,v) = Σᵢ Σⱼ Bᵢ(u) Bⱼ(v) Pᵢⱼ
A grid of control points, with the curve basis applied in each direction.
S(u,v) = Σᵢ Bᵢ(u) · [ Σⱼ Bⱼ(v) Pᵢⱼ ]
Evaluate as curves in v, then one curve through the results.
bicubic: 4×4 = 16 control points
The standard patch. Enough for C² joins in both directions.
Evaluation is just the curve algorithm applied twice, which means de Casteljau and de Boor transfer directly.
CSCE 645 · Geometric Modeling — Module 05
3
Notes: The nested evaluation is how you actually implement it, and it makes the cost obvious: (p+1) curve evaluations plus one more.

## Slide 5
EVALUATION
Nested de Casteljau
cpp
vec3 eval_patch(const vec3 P[4][4], float u, float v) {
vec3 row[4];
for (int i = 0; i < 4; i++)
row[i] = de_casteljau({P[i][0], P[i][1], P[i][2], P[i][3]}, v);
return de_casteljau({row[0], row[1], row[2], row[3]}, u);
}
// Partial derivatives for the normal: differentiate one direction,
// evaluate the other.
vec3 n = normalize(cross(dSdu(P,u,v), dSdv(P,u,v)));
// -> ANALYTIC normals, exact at every point. Meshes cannot do this.
Exact analytic normals are a real advantage of parametric surfaces — no averaging, no tessellation dependence.
CSCE 645 · Geometric Modeling — Module 05
4
Notes: Tie back to Module 02's normal-weighting discussion: that whole problem does not exist here.

## Slide 6
PART 2
The limitation
A grid of control points implies a grid of topology.
CSCE 645 · Geometric Modeling — Module 05
5

## Slide 7
Tensor products force quad topology
THE STRUCTURAL PROBLEM
The construction needs a rectangular grid of control points. That is what 'tensor product' means.
So a single patch is topologically a square. Any surface built from them is a quad mesh of patches.
A sphere needs at least two patches and has degenerate poles. A torus works. A character's head, with its natural five- and three-valence vertices, does not fit at all.
Every difficulty in the rest of this module descends from this one fact.
CSCE 645 · Geometric Modeling — Module 05
6

## Slide 8
TRIMMING
Holes, and the price of them
▪ Want a hole in a patch? You cannot remove control points — the grid must stay rectangular.
▪ Trimming: keep the patch, and carry curves in parameter space marking which regions are valid.
▪ Now every operation must respect the trim curves:
  – Tessellation must triangulate a region bounded by curves, not a rectangle.
  – Two trimmed patches meeting at an edge rarely match exactly — hence gaps.
▪ Trimming is where CAD kernels spend much of their complexity and most of their bugs.
CSCE 645 · Geometric Modeling — Module 05
7
Notes: The gap problem is why CAD-to-mesh export is notoriously unreliable. Worth saying plainly.

## Slide 9
PART 3
Cross-patch continuity
Making two patches meet smoothly is harder than it looks.
CSCE 645 · Geometric Modeling — Module 05
8

## Slide 10
CONTINUITY
Conditions across a patch boundary
Want
Requires
Difficulty
C⁰
Shared boundary control points
Easy
G¹
Boundary tangent planes agree along the whole edge
Doable
G²
Curvature agrees along the whole edge
Hard
At a corner
All meeting patches agree — the vertex enclosure problem
Often impossible
CSCE 645 · Geometric Modeling — Module 05
9
Notes: The corner case is the killer. For odd numbers of patches meeting at a point, G1 can be unachievable with the obvious construction.

## Slide 11
The vertex enclosure problem
WHY THIS APPROACH RUNS OUT
Making two patches meet smoothly along an edge is manageable. Making n patches meet smoothly at a corner is a different matter.
The tangent plane conditions along each of the n shared edges must all be mutually consistent at the shared vertex. For certain valences — particularly odd ones — the resulting system has no solution with the obvious patch degree.
Workarounds exist: raise the degree, split patches, or accept approximate continuity. All add complexity, and all are why patch-based modelling of organic shapes is painful.
Subdivision surfaces (Module 06) sidestep this entirely by never forming explicit patches. That is their central advantage.
CSCE 645 · Geometric Modeling — Module 05
10

## Slide 12
WHERE PATCHES WORK
An honest assessment
▪ Work well: engineered parts, surfaces of revolution, extrusions, lofts, anything naturally rectangular.
▪ Work well: exact representation and manufacturing tolerance — NURBS is the only serious option.
▪ Work badly: arbitrary topology, organic shapes, anything with irregular vertices.
▪ Work badly: local refinement — adding detail means inserting an entire row or column.
▪ That last point matters: T-splines and hierarchical B-splines exist specifically to allow local refinement.
CSCE 645 · Geometric Modeling — Module 05
11

## Slide 13
PRACTICE
Tessellating a patch for rendering
cpp
// Uniform: simple, and wastes triangles on flat regions.
for (i = 0; i <= N; i++)
for (j = 0; j <= N; j++)
vertex[i][j] = eval_patch(P, i/(float)N, j/(float)N);
// Adaptive: subdivide where curvature is high, as in Module 03.
// Screen-space error is the right criterion -- a patch covering
// 10 pixels needs no more than 10 pixels' worth of triangles.
// Hardware tessellation (CSCE 641 Module 12) evaluates patches
// on the GPU: the control cage is the vertex buffer, and the
// tessellation evaluation shader computes S(u,v).
This is the direct connection to CSCE 641: GPU tessellation exists to evaluate exactly these surfaces at render time.
CSCE 645 · Geometric Modeling — Module 05
12
Notes: Closing the loop with 641's tessellation module makes both land better.

## Slide 14
What to carry forward
1. A tensor-product surface applies a curve basis in each parameter direction, over a rectangular grid of control points.
2. Evaluation is the curve algorithm nested: evaluate rows, then evaluate across the results.
3. Parametric surfaces give exact analytic normals, which meshes cannot — no averaging and no tessellation dependence.
4. The construction forces quadrilateral topology. Every later difficulty descends from that.
5. Trimming adds holes by marking invalid regions in parameter space, and is where CAD kernels keep most of their complexity and their gaps.
6. The vertex enclosure problem makes smooth corners between many patches hard or impossible — which is what subdivision surfaces avoid.
CSCE 645 · Geometric Modeling — Module 05
13