## Slide 1
UNIVERSITY OF CLAUDE
CSCE 649 — Physically-Based Modeling
MODULE 09
Deformable Solids
Continuum mechanics, and why mass-spring was never going to work.
CSCE 649 · Module 09 of 13 · original material, share freely

## Slide 2
MODULE OUTCOMES
What you will be able to do
▪ Define strain and stress and explain what each measures.
▪ Explain why linear elasticity fails under rotation.
▪ Implement corotational FEM.
▪ Handle element inversion.
▪ Choose between FEM, mass-spring, and shape matching.
CSCE 649 · Physically-Based Modeling — Module 09
1
Notes: State the outcomes before the content. Every slide that follows exists to serve one of these.

## Slide 3
PART 1
Strain
Measuring deformation without measuring motion.
CSCE 649 · Physically-Based Modeling — Module 09
2

## Slide 4
The central problem: rotation is not deformation
WHAT STRAIN MUST ACHIEVE
Rotate a rubber block by 90°. Every vertex has moved a long way. The material has not deformed at all.
A strain measure must report zero for any rigid motion — translation or rotation — and non-zero only for genuine stretching, compression, or shear.
Mass-spring models fail this test. A spring sees only distance between endpoints, which is why a mass-spring cube can be inverted with every spring at rest length.
Getting this right is what continuum mechanics buys, and it is the whole reason this module exists.
CSCE 649 · Physically-Based Modeling — Module 09
3

## Slide 5
DEFORMATION
The deformation gradient
F = ∂x / ∂X
How deformed positions x change with material positions X. A 3×3 matrix per element. Everything derives from it.
ε = ½(F + Fᵀ) − I
Linear (Cauchy) strain. Cheap — and WRONG under rotation.
E = ½(FᵀF − I)
Green strain. Exactly zero for any rotation, because RᵀR = I. Nonlinear in the displacements.
FᵀF removes the rotation because rotations are orthogonal. That one identity is the whole trick.
CSCE 649 · Physically-Based Modeling — Module 09
4
Notes: Show RᵀR = I explicitly. The reason Green strain works is a one-line observation.

## Slide 6
Linear strain fails visibly, and famously
THE ARTEFACT EVERYONE HAS SEEN
Cauchy strain is linear in displacement, which makes the solver a single linear system — fast and easy.
It reports non-zero strain for a pure rotation, so the material resists being rotated.
The visible result is ghost forces and volume growth: an arm rotating at the shoulder inflates. This is the classic linear-FEM artefact.
It is fine for small deformations — a loaded beam, a vibrating plate. It is useless for animation, where everything rotates.
CSCE 649 · Physically-Based Modeling — Module 09
5

## Slide 7
PART 2
Stress and energy
From deformation to force.
CSCE 649 · Physically-Based Modeling — Module 09
6

## Slide 8
MODELS
Constitutive models
Model
Description
Use
St. Venant–Kirchhoff
Linear stress from Green strain
Collapses under compression
Neo-Hookean
Nonlinear; resists compression strongly
The usual choice
Mooney–Rivlin
More parameters, better fits
Matching measured rubber
Corotational
Linear, with rotation factored out
Fast, stable, good enough
CSCE 649 · Physically-Based Modeling — Module 09
7
Notes: That the parameters are real measurable quantities is the practical payoff over mass-spring.

## Slide 9
PARAMETERS
Real material parameters
E — Young's modulus
Resistance to stretching, in pascals. Rubber ≈ 10⁷; steel ≈ 2×10¹¹.
ν — Poisson's ratio
How much it bulges sideways when squeezed. 0.5 is incompressible; rubber ≈ 0.49.
Look them up, do not tune them
Unlike spring constants, these are published for real materials and transfer across meshes.
ν near 0.5 makes the system nearly incompressible, which is numerically hard. 0.45 is the usual compromise.
CSCE 649 · Physically-Based Modeling — Module 09
8
Notes: The locking problem at ν→0.5 is worth mentioning — it is why nobody uses 0.499.

## Slide 10
PART 3
Corotational FEM
The method that made deformables practical.
CSCE 649 · Physically-Based Modeling — Module 09
9

## Slide 11
COROTATIONAL
Factor out the rotation, then go linear
cpp
// Per element, per step:
for (auto& e : elements) {
// 1. Deformation gradient from the current vertex positions.
mat3 F = compute_F(e, x);
// 2. Polar decomposition F = R * S. R is the rotation part;
// S is the symmetric stretch part. THIS is the key step.
mat3 R = polar_decomposition_rotation(F);
// 3. Rotate the element back to its rest orientation, apply the
// cheap LINEAR model there, then rotate the forces forward.
// Linear elasticity is correct when there is no rotation left.
mat3 Fhat = R.transpose() * F; // rotation removed
mat3 P = linear_stress(Fhat); // cheap and now valid
accumulate_forces(e, R * P); // rotate forces back
}
// Cost: one polar decomposition per element per step. Result: linear
// elasticity's speed with none of its rotation artefacts.
Linear elasticity is wrong only because of rotation. Remove the rotation and it becomes correct again.
CSCE 649 · Physically-Based Modeling — Module 09
10
Notes: The insight is almost embarrassingly simple and it is why corotational FEM is everywhere.

## Slide 12
Polar decomposition is the whole method
WHY IT WORKS
Any deformation gradient F factors as F = R·S: a rotation followed by a symmetric stretch.
R is the rotation the element has undergone; S is the actual deformation.
Linear elasticity is accurate for small deformation with no rotation. Factor R out and that condition is satisfied, so the cheap model becomes valid.
Cost is one polar decomposition per element per step — a few iterations of a simple algorithm, or a closed form in 3D. You get linear speed with nonlinear correctness under rotation.
CSCE 649 · Physically-Based Modeling — Module 09
11

## Slide 13
Inverted elements must be handled, not prevented
THE ROBUSTNESS PROBLEM
Under a large impact a tetrahedron can turn inside out: det F < 0.
Most models produce garbage there. Forces point the wrong way, the element inverts further, and the simulation fails.
You cannot reliably prevent it, so handle it: Irving, Teran and Fedkiw's method clamps the singular values of F and extends the model smoothly into the inverted regime, so forces push the element back out.
Without this, a deformable simulation is one bad frame away from failure. With it, inversion is recoverable and often invisible.
CSCE 649 · Physically-Based Modeling — Module 09
12

## Slide 14
PART 4
Alternatives
What else is used, and when.
CSCE 649 · Physically-Based Modeling — Module 09
13

## Slide 15
COMPARISON
Three approaches
Method
Strength
Weakness
FEM
Real parameters; converges with mesh
Complex; needs a solver
Mass-spring
Trivial to implement; fast
Mesh-dependent; no volume
Shape matching
Unconditionally stable; very fast
Not a material model
MPM
Handles topology change, plasticity
Expensive; grid artefacts
CSCE 649 · Physically-Based Modeling — Module 09
14
Notes: MPM is covered in Module 12. Mention it here as the topology-change answer.

## Slide 16
Why FEM beats mass-spring, concretely
THE CASE
Parameters are real. Young's modulus for rubber is published. There is no published spring constant for rubber.
Behaviour converges with mesh refinement rather than changing, so a finer mesh is more detail and not a different material.
Volume is represented. An element knows it has been inverted; a spring network does not.
Anisotropy can be specified rather than emerging from the triangulation.
The cost is a linear solve per step and considerably more implementation. For anything that must behave like a specific material, it is worth it.
CSCE 649 · Physically-Based Modeling — Module 09
15

## Slide 17
What to carry forward
1. A strain measure must report zero for any rigid motion. Mass-spring models fail this, which is their fundamental defect.
2. Everything derives from the deformation gradient F. Green strain ½(FᵀF − I) is zero under rotation because RᵀR = I.
3. Linear Cauchy strain is cheap and reports non-zero strain for pure rotation, which produces ghost forces and inflating limbs.
4. Material parameters are Young's modulus and Poisson's ratio — measurable, published, and transferable, unlike spring constants.
5. Corotational FEM polar-decomposes F = R·S, removes the rotation, and applies the cheap linear model where it is valid.
6. Element inversion cannot be prevented, only handled — clamp the singular values and extend the model into the inverted regime.
CSCE 649 · Physically-Based Modeling — Module 09
16