## Slide 1
UNIVERSITY OF CLAUDE
CSCE 650 — Virtual Reality
MODULE 02
Human Vision for VR
The specification you are actually building against.
CSCE 650 · Module 02 of 13 · original material, share freely

## Slide 2
MODULE OUTCOMES
What you will be able to do
▪ State the relevant limits of human vision in numbers.
▪ Explain acuity falloff and what it permits.
▪ Distinguish the depth cues and say which VR provides.
▪ Explain the vergence-accommodation conflict.
▪ Explain flicker fusion and persistence.
CSCE 650 · Virtual Reality — Module 02
1
Notes: State the outcomes before the content. Every slide that follows exists to serve one of these.

## Slide 3
PART 1
The numbers
What the eye actually resolves.
CSCE 650 · Virtual Reality — Module 02
2

## Slide 4
VISION
The specification
Property
Human
Consumer headset
Horizontal FOV
~200° binocular
~100–110°
Foveal acuity
~60 pixels/degree
~15–35 ppd
Acuity at 20°
~10 pixels/degree
Same as centre — wasteful
Flicker fusion
60–90 Hz, higher in periphery
72–120 Hz
Stereo depth limit
~10 m useful
Beyond that, monocular cues
CSCE 650 · Virtual Reality — Module 02
3
Notes: These numbers anchor every later decision. Have them memorise the acuity figure at least.

## Slide 5
Acuity collapses outside the fovea
THE FACT THAT FOVEATED RENDERING EXPLOITS
The fovea is about 2° wide — roughly a thumbnail at arm's length — and is where all detailed vision happens.
At 20° off-axis, acuity is about a sixth of foveal. At 40° it is far worse still.
Yet a headset renders the entire field at uniform resolution, which means the overwhelming majority of pixels are far more detailed than the eye can use.
Foveated rendering (Module 10) recovers that waste — and the reason it works is entirely this slide.
CSCE 650 · Virtual Reality — Module 02
4

## Slide 6
You do not perceive the periphery the way you think
A USEFUL DEMONSTRATION
Hold up a playing card at arm's length, look straight ahead, and move it sideways. You cannot identify it past about 10° — yet the world does not appear blurry.
The brain fills in, using memory, saccades, and assumption. The vivid detailed field you experience is largely constructed.
But the periphery is extremely sensitive to motion and flicker — more so than the fovea.
So: detail can be cut in the periphery; motion and flicker cannot. That asymmetry governs both foveated rendering and comfort design.
CSCE 650 · Virtual Reality — Module 02
5

## Slide 7
PART 2
Depth
Many cues, and VR provides some of them.
CSCE 650 · Virtual Reality — Module 02
6

## Slide 8
DEPTH CUES
How depth is perceived
Cue
Range
VR provides?
Stereopsis
To ~10 m
Yes — the headline feature
Motion parallax
All
Yes — and underrated
Vergence
To ~2 m
Yes, and conflicted
Accommodation
To ~2 m
No — fixed focal plane
Occlusion
All
Yes
Relative size, perspective
All
Yes
Shading, shadows
All
Yes — cheap and effective
CSCE 650 · Virtual Reality — Module 02
7
Notes: Students over-weight stereopsis. Parallax from head motion is what makes a space feel real.

## Slide 9
The vergence-accommodation conflict
THE UNSOLVED HARDWARE PROBLEM
Vergence: the eyes rotate inward to converge on an object. Accommodation: the lens changes shape to focus at that distance.
In the real world they are coupled — the brain uses each as a cue for the other, and they always agree.
In a headset the display is at a fixed optical distance — typically 1.5 to 2 m. So the eyes verge on a virtual object at 30 cm while still accommodating at 2 m.
The conflict causes eye strain and fatigue, and it is why close-up work is uncomfortable. No shipping headset solves it; varifocal and light-field displays are the research directions.
CSCE 650 · Virtual Reality — Module 02
8

## Slide 10
MITIGATION
Designing around the conflict
▪ Keep interactive content at 0.5–2 m, near the display's focal distance. This is the single most effective measure.
▪ Avoid sustained close work. Text at 30 cm is uncomfortable within minutes.
▪ Put UI at a comfortable depth and keep it there. UI that floats at a different depth from what it labels is tiring.
▪ Reduce stereo separation for very close objects if you must have them — physically wrong, and more comfortable.
▪ Do not put anything closer than ~20 cm. Fusion fails and the image doubles.
CSCE 650 · Virtual Reality — Module 02
9
Notes: The 0.5-2 m rule is the practical takeaway and explains a lot of VR UI design.

## Slide 11
PART 3
Time
Flicker, persistence, and motion.
CSCE 650 · Virtual Reality — Module 02
10

## Slide 12
Low persistence is why modern VR is not a smeared mess
THE KEY DISPLAY INSIGHT
A full-persistence display holds each frame lit for the whole frame period. During head motion, the eye moves across a stationary image, and the result smears.
Low-persistence displays illuminate for ~2 ms and are dark the rest of the time — so the image is a brief flash at a definite position.
Motion blur from eye movement disappears. This was one of the decisive changes between early and modern headsets.
The cost is brightness and flicker. Lit 2 ms in 11 is dim, and the flicker is visible in the periphery at lower rates — which is one reason 90 Hz rather than 72.
CSCE 650 · Virtual Reality — Module 02
11

## Slide 13
CONSEQUENCES
What follows for rendering
▪ Do not add motion blur. The display's low persistence exists to remove blur; adding it back is perverse and adds perceived latency.
▪ Be careful with temporal antialiasing. It smears during head motion, which is constant, and the smear reads as latency.
▪ MSAA is often the right choice in VR despite being unfashionable, because it does not accumulate across frames.
▪ Flickering content is worse in the periphery, where sensitivity is highest. Avoid high-frequency flicker anywhere, and especially at the edges.
▪ High-contrast edges in the periphery induce vection (Module 07) and therefore sickness.
The MSAA point reverses a decade of real-time rendering practice, and the reason is persistence.
CSCE 650 · Virtual Reality — Module 02
12

## Slide 14
Binocular rivalry: the eyes must agree
A FAILURE MODE TO KNOW
If the two eyes receive sufficiently different images, the brain does not blend them. It alternates between them, which is deeply unpleasant.
Causes: an effect rendered in one eye only, a view-dependent effect computed from the wrong eye, a UI element with incorrect disparity.
Specular highlights and reflections legitimately differ between eyes — that is correct and fine. Gross differences are not.
Test by closing one eye, then the other. If the two images differ in anything but viewpoint, something is wrong.
CSCE 650 · Virtual Reality — Module 02
13

## Slide 15
What to carry forward
1. Foveal acuity is about 60 pixels per degree over a ~200° field; consumer headsets deliver 15–35 ppd over ~110°.
2. Acuity collapses outside the 2° fovea — about a sixth at 20° — which is the entire basis of foveated rendering.
3. The periphery is poor at detail and excellent at motion and flicker, so cut detail there and never flicker.
4. Stereopsis gets the attention; motion parallax does more work, and shadows are the cheapest depth cue available.
5. Vergence and accommodation are coupled in reality and decoupled in a headset, causing fatigue. Keep interactive content between 0.5 and 2 m.
6. Low-persistence displays flash each frame for ~2 ms, removing eye-motion smear — so do not add motion blur back, and prefer MSAA to heavy TAA.
CSCE 650 · Virtual Reality — Module 02
14