## Slide 1
UNIVERSITY OF CLAUDE
CSCE 650 — Virtual Reality
MODULE 04
Display Optics and Distortion
What the lens does, and what you must undo.
CSCE 650 · Module 04 of 13 · original material, share freely

## Slide 2
MODULE OUTCOMES
What you will be able to do
▪ Explain why HMDs need lenses at all.
▪ Explain barrel and pincushion distortion and the correction order.
▪ Explain chromatic aberration correction.
▪ Explain why distortion must happen after timewarp.
▪ Name the display artefacts and their causes.
CSCE 650 · Virtual Reality — Module 04
1
Notes: State the outcomes before the content. Every slide that follows exists to serve one of these.

## Slide 3
PART 1
Why a lens
The display is 3 cm from your eye.
CSCE 650 · Virtual Reality — Module 04
2

## Slide 4
You cannot focus on a screen 3 cm away
THE PROBLEM THE LENS SOLVES
The nearest an adult eye can focus is roughly 10 cm, and it is uncomfortable well before that. A headset display sits 3 to 5 cm from the eye.
The lens makes the display appear to be at 1.5 to 2 m, where the eye is relaxed.
It also magnifies, so a small panel fills a wide field of view — which is the other reason it is there.
And it introduces distortion, chromatic aberration, and a fixed focal plane, which are Modules 04 and 02's problems respectively. The lens creates as many problems as it solves.
CSCE 650 · Virtual Reality — Module 04
3

## Slide 5
DISTORTION
Barrel and pincushion
The lens produces pincushion
▪ Magnification increases with distance from the axis.
▪ Straight lines bow inward at the edges.
▪ A property of the optics — unavoidable.
  – Worse with wider fields of view.
So you render barrel
▪ Pre-distort the image the opposite way.
▪ Straight lines bow outward in the submitted frame.
▪ The two cancel, and the user sees straight lines.
  – Which is why a raw VR frame looks wrong on a monitor.
CSCE 650 · Virtual Reality — Module 04
4
Notes: The 'raw frame looks wrong' point is how students first encounter this, usually in a screenshot.

## Slide 6
Chromatic aberration is corrected per channel
THREE DISTORTIONS, NOT ONE
A lens refracts different wavelengths by different amounts, so red, green, and blue focus at slightly different magnifications.
Uncorrected, this appears as coloured fringing at the edges of the field — a red or blue halo on high-contrast edges.
The correction applies a slightly different distortion mesh to each colour channel.
It is never perfect, which is why you can still see fringing at the extreme edges of most headsets if you look for it.
CSCE 650 · Virtual Reality — Module 04
5

## Slide 7
PART 2
Where distortion happens
And why the order is not negotiable.
CSCE 650 · Virtual Reality — Module 04
6

## Slide 8
ORDER
The compositor pipeline
text
APPLICATION COMPOSITOR (the runtime)
----------- ------------------------
1. predict head pose
2. render left eye ---------->
3. render right eye ----------> 4. take the LATEST head pose
(submit undistorted, (newer than step 1's)
flat, linear images) 5. TIMEWARP: reproject the
submitted image to it
6. apply LENS DISTORTION
(per colour channel)
7. scan out to the display
*** DISTORTION MUST COME AFTER TIMEWARP. ***
Timewarp is a rotation in the undistorted image space. Applying
it to an already-distorted image warps the distortion itself,
and the correction no longer matches the lens.
You submit flat, undistorted images. The compositor owns steps 4 to 7, and the ordering is the reason.
CSCE 650 · Virtual Reality — Module 04
7
Notes: This slide answers 'why can't I just do the distortion myself' — which students ask, and the answer is timewarp.

## Slide 9
Do not implement your own distortion
THE PRACTICAL RULE
The distortion mesh is device-specific and sometimes unit-specific, derived from factory calibration of the actual lenses.
It must compose correctly with timewarp, which the compositor applies after you are finished.
And it changes with eye relief and IPD — the correction depends on where the eye actually is.
Submit flat undistorted images and let the runtime do it. Early VR required applications to distort; OpenXR exists partly so they no longer have to.
CSCE 650 · Virtual Reality — Module 04
8

## Slide 10
PART 3
Consequences for rendering
Distortion is not free, and it changes pixel density.
CSCE 650 · Virtual Reality — Module 04
9

## Slide 11
Distortion compresses the periphery
WHERE YOUR PIXELS GO
Barrel pre-distortion stretches the centre and compresses the edges of the submitted image.
So peripheral pixels you rendered are thrown away — several submitted pixels collapse into one displayed pixel at the edges.
And central pixels are stretched, so the submitted image must be rendered larger than the display to keep the centre sharp.
That is why the recommended render target exceeds the panel resolution, often by 30–40%. You are rendering extra pixels so that the centre survives the warp.
CSCE 650 · Virtual Reality — Module 04
10

## Slide 12
EXPLOIT IT
Techniques that follow
▪ Radial density masking: skip rendering the corners entirely — they are outside the visible lens area.
▪ A stencil mesh supplied by the runtime marks the pixels that will never be seen. Free performance; apply it.
▪ Fixed foveated rendering (Module 10) reduces shading rate toward the edges, which the distortion is going to compress anyway.
▪ Lower-resolution periphery matches both the distortion and the eye's acuity falloff (Module 02). The two agree, which is convenient.
The hidden area mesh is the single easiest VR performance win and is frequently left unapplied.
CSCE 650 · Virtual Reality — Module 04
11

## Slide 13
ARTEFACTS
Display artefacts and their causes
Artefact
Cause
Screen door
Visible gaps between pixels; fill factor
Mura
Per-pixel brightness variation; panel manufacturing
God rays
Internal reflection in Fresnel lenses; bright on dark
Chromatic fringing
Imperfect aberration correction at the edges
Pupil swim
Distortion is wrong when the eye moves off-axis
Glare, ghosting
Lens surface reflections
CSCE 650 · Virtual Reality — Module 04
12
Notes: Pupil swim is the subtle one — distortion is calibrated for a fixed eye position and the eye rotates.

## Slide 14
Pupil swim, and why eye tracking helps
THE RESIDUAL ERROR
The distortion correction is calibrated for the eye at one position — looking straight ahead, at a nominal eye relief.
When the eye rotates, the pupil moves, and the correction is no longer exactly right.
The world appears to warp slightly as you look around — subtle, and a real contributor to the sense that something is not quite solid.
Eye tracking allows dynamic distortion correction, adjusting the mesh for the current gaze. This is one of the less-discussed benefits of eye tracking and may matter more than foveated rendering.
CSCE 650 · Virtual Reality — Module 04
13

## Slide 15
What to carry forward
1. A lens is needed because the eye cannot focus at 3 cm; it also magnifies, and it introduces distortion, aberration, and a fixed focal plane.
2. The lens produces pincushion distortion, so the application's image is pre-distorted with barrel distortion and the two cancel.
3. Chromatic aberration is corrected with a slightly different mesh per colour channel, and never perfectly.
4. Distortion must be applied after timewarp, because timewarp operates in undistorted image space — which is why the compositor owns it.
5. Pre-distortion compresses the periphery and stretches the centre, which is why the recommended render target exceeds the panel resolution.
6. Apply the runtime's hidden-area stencil mesh — it is the easiest VR performance win and is routinely left on the table.
CSCE 650 · Virtual Reality — Module 04
14