## Slide 1
UNIVERSITY OF CLAUDE
CSCE 650 — Virtual Reality
MODULE 05
Tracking
Knowing where the head is, continuously and without drift.
CSCE 650 · Module 05 of 13 · original material, share freely

## Slide 2
MODULE OUTCOMES
What you will be able to do
▪ Explain what an IMU measures and why it drifts.
▪ Explain sensor fusion and the role of each sensor.
▪ Compare inside-out and outside-in tracking.
▪ Explain prediction and why it is necessary.
▪ Explain tracking failure modes and how to handle them.
CSCE 650 · Virtual Reality — Module 05
1
Notes: State the outcomes before the content. Every slide that follows exists to serve one of these.

## Slide 3
PART 1
The IMU
Fast, and it drifts.
CSCE 650 · Virtual Reality — Module 05
2

## Slide 4
SENSORS
What an IMU actually measures
Sensor
Measures
Problem
Gyroscope
Angular velocity
Integrate once → drift
Accelerometer
Linear acceleration + gravity
Integrate twice → drift fast
Magnetometer
Magnetic field direction
Distorted by metal, speakers
CSCE 650 · Virtual Reality — Module 05
3
Notes: The 'integrate twice' point explains why position tracking needs cameras and orientation nearly does not.

## Slide 5
Double integration is why position drifts so fast
THE ARITHMETIC
Orientation comes from integrating angular velocity once. A small bias accumulates linearly — degrees per minute.
Position comes from integrating acceleration twice. A small bias accumulates quadratically — and gravity is a 9.8 m/s² signal you must subtract perfectly.
An accelerometer bias of 0.01 m/s² gives half a metre of error in ten seconds.
So inertial position tracking alone is hopeless, and every system corrects it with an optical reference. The IMU provides the rate; the cameras provide the truth.
CSCE 650 · Virtual Reality — Module 05
4

## Slide 6
PART 2
Fusion
Fast and drifting, plus slow and absolute.
CSCE 650 · Virtual Reality — Module 05
5

## Slide 7
COMPLEMENTARY
The two halves
IMU
▪ 1000 Hz, latency under a millisecond.
▪ Smooth, no jitter.
▪ Drifts — no absolute reference.
  – Tells you how you are moving right now.
Optical (cameras)
▪ 30–90 Hz, tens of milliseconds of latency.
▪ Noisy, and can fail entirely.
▪ Absolute — no drift.
  – Tells you where you actually are, late.
CSCE 650 · Virtual Reality — Module 05
6
Notes: The complementarity is exact: each sensor's weakness is the other's strength. That is what makes fusion work so well.

## Slide 8
The fusion principle
HOW THE TWO ARE COMBINED
Use the IMU for high-frequency motion — it is fast, smooth, and correct over short intervals.
Use the optical estimate to correct low-frequency drift — it is slow and absolute.
A complementary filter is the simple version; an extended or unscented Kalman filter is the usual production answer, estimating sensor biases as part of the state.
The output is better than either sensor alone by a wide margin, which is the standard result for complementary sensors and the reason every tracking system looks like this.
CSCE 650 · Virtual Reality — Module 05
7

## Slide 9
TOPOLOGY
Inside-out and outside-in
Outside-in
Inside-out
Cameras
Fixed in the room
On the headset
Tracks
Markers on the headset
Features in the room
Accuracy
Higher; well-conditioned
Good; depends on the room
Setup
Base stations required
None
Play space
Bounded by the stations
Unbounded
Fails when
Occluded by your body
Blank walls; poor light
CSCE 650 · Virtual Reality — Module 05
8
Notes: The blank-wall failure is worth knowing: a featureless white room is genuinely hard for inside-out tracking.

## Slide 10
PART 3
Prediction
Rendering for where the head will be.
CSCE 650 · Virtual Reality — Module 05
9

## Slide 11
You must render for the future
WHY PREDICTION IS NOT OPTIONAL
By the time a frame reaches the display, the pose used to render it is tens of milliseconds old (Module 06).
So the runtime predicts where the head will be at the moment of photon emission, and you render for that pose.
Short-horizon prediction is remarkably accurate, because heads have mass and cannot change direction instantly — 20 to 40 ms ahead is reliable.
Beyond that it degrades, and overshoot during direction changes produces a characteristic swimming sensation. This is the limit on how much latency prediction can hide.
CSCE 650 · Virtual Reality — Module 05
10

## Slide 12
USING IT
Prediction in practice
▪ Ask the runtime for the pose at the predicted display time, not for the current pose. OpenXR's API is built around this.
▪ Use the same predicted pose for both eyes and for all rendering in the frame. Mixing poses within a frame produces inconsistency.
▪ Late latching reads the pose as late as possible — after the CPU work, just before the GPU needs it.
▪ Do not predict further than necessary. Longer horizons mean larger errors, and timewarp (Module 06) handles the residual better than prediction does.
CSCE 650 · Virtual Reality — Module 05
11
Notes: The 'same pose for everything in the frame' rule catches people who query the pose per object.

## Slide 13
Tracking loss must be handled, not ignored
THE DESIGN REQUIREMENT
Tracking will fail. Occlusion, a featureless wall, direct sunlight, a user covering a camera with their hand.
Snapping the view to a default pose is the worst possible response — an unrequested instantaneous viewpoint change is maximally disorienting.
Degrade gracefully: fall back to orientation-only tracking, hold the last known position, and fade the world out if it persists.
Tell the user. A clear indication that tracking is lost is far better than a world that behaves inexplicably.
CSCE 650 · Virtual Reality — Module 05
12

## Slide 14
FAILURE
What makes tracking fail
▪ Featureless surfaces. A blank white wall gives inside-out tracking nothing to lock onto.
▪ Poor or changing light. Cameras need photons; a dark room is hard and a flickering one is worse.
▪ Repetitive texture. A tiled floor or a regular brick wall produces false matches.
▪ Moving environments. A train, a car, or a boat — the IMU reports the vehicle's acceleration as the head's.
▪ Occlusion of controllers behind the body or outside the camera field, which is constant in practice.
Vehicles are a genuine unsolved case, and the reason VR on a train is unpleasant.
CSCE 650 · Virtual Reality — Module 05
13

## Slide 15
What to carry forward
1. A gyroscope measures angular velocity and an accelerometer measures acceleration plus gravity. Neither measures position.
2. Orientation integrates once and drifts linearly; position integrates twice and drifts quadratically — so inertial position tracking alone is hopeless.
3. IMU and cameras are exactly complementary: fast and drifting against slow and absolute. Fusion is better than either by a wide margin.
4. Inside-out tracking won on convenience; its failure modes are blank walls, poor light, and repetitive texture rather than occlusion.
5. You must render for a predicted future pose. Prediction is reliable to 20–40 ms because heads have mass.
6. Tracking loss must degrade gracefully — never snap to a default pose, and tell the user what happened.
CSCE 650 · Virtual Reality — Module 05
14