## Slide 1
UNIVERSITY OF CLAUDE
CSCE 650 — Virtual Reality
MODULE 06
Latency
The central problem, and everything built to hide it.
CSCE 650 · Module 06 of 13 · original material, share freely

## Slide 2
MODULE OUTCOMES
What you will be able to do
▪ Account for every stage of the motion-to-photon budget.
▪ State the latency threshold and what exceeding it does.
▪ Explain timewarp and what it can and cannot correct.
▪ Explain spacewarp and its artefacts.
▪ Measure latency rather than estimating it.
CSCE 650 · Virtual Reality — Module 06
1
Notes: State the outcomes before the content. Every slide that follows exists to serve one of these.

## Slide 3
PART 1
The budget
Motion to photon, stage by stage.
CSCE 650 · Virtual Reality — Module 06
2

## Slide 4
PIPELINE
Where the milliseconds go
Stage
Typical
Can you reduce it?
Sensor sampling
1 ms
No
Fusion and pose
1 ms
No
Application CPU
2–11 ms
Yes — this is yours
Application GPU
2–11 ms
Yes — this is yours
Compositor
1–2 ms
No
Scan-out
Up to 11 ms
Higher refresh rate only
Pixel response
1–3 ms
Panel technology
CSCE 650 · Virtual Reality — Module 06
3
Notes: The point of the table is that the application owns maybe half the budget and must be ruthless with it.

## Slide 5
20 ms is the threshold, and it is not a preference
WHAT THE RESEARCH SAYS
Below roughly 20 ms motion-to-photon, the world feels attached to the room. Above it, it feels attached to your head, and lags.
People detect latency differences down to a few milliseconds in controlled tests, well below the threshold at which they can describe what is wrong.
And the symptom is not 'it feels laggy' — it is discomfort, disorientation, and eventually nausea (Module 07).
This single number drove the entire architecture of modern VR: low persistence, timewarp, prediction, and the compositor all exist to get under it.
CSCE 650 · Virtual Reality — Module 06
4

## Slide 6
PART 2
Timewarp
The most important trick in VR.
CSCE 650 · Virtual Reality — Module 06
5

## Slide 7
Reproject the finished frame to a newer pose
HOW TIMEWARP WORKS
The application renders from a pose predicted some milliseconds ago. Before scan-out, the compositor takes a fresh pose — much newer — and reprojects the finished image to it.
For rotation this is nearly exact, because rotating the view of a distant scene is a simple image warp with no missing information.
It cuts effective latency enormously — the user's rotation is reflected with only the compositor's own latency.
And it is why head rotation feels solid even when the application is struggling. Rotation is the dominant head motion, so this covers most of the problem.
CSCE 650 · Virtual Reality — Module 06
6

## Slide 8
LIMITS
What timewarp can and cannot fix
Rotation — handled well
▪ A pure rotation of the view.
▪ No information is missing — the same scene, seen from the same point, rotated.
▪ Edges of the field may lack data; the render target is oversized to cover it.
  – Nearly exact.
Translation — handled badly
▪ The head moves to a new position.
▪ Parallax changes — you would see behind objects, and that data was never rendered.
▪ Requires a depth buffer and still leaves holes.
  – Positional timewarp exists and is approximate.
CSCE 650 · Virtual Reality — Module 06
7
Notes: The rotation/translation asymmetry is the key limitation and explains why translation latency matters more.

## Slide 9
Asynchronous timewarp runs whether you finish or not
THE SAFETY NET
ATW runs on its own schedule, in a high-priority context, and reprojects whatever the most recent complete frame is.
So a missed frame does not mean a repeated frame. The old frame is re-warped to the current pose, and head rotation stays correct.
The world stays stable; moving objects stutter. Which is a far better failure than the whole world juddering.
It is a safety net, not a licence. Shipping an application that relies on ATW to hit its rate means every animation runs at half rate, which users notice.
CSCE 650 · Virtual Reality — Module 06
8

## Slide 10
PART 3
Spacewarp
Synthesising frames you did not render.
CSCE 650 · Virtual Reality — Module 06
9

## Slide 11
Spacewarp extrapolates motion, with artefacts
WHAT IT COSTS
Asynchronous spacewarp generates an entirely new frame by extrapolating object motion from previous frames, using motion vectors and depth.
So an application running at 45 Hz can present at 90, with synthesised alternate frames.
The artefacts are characteristic: wobbling at object edges, smearing behind fast movers, and disocclusion holes where background was never rendered.
Supply accurate motion vectors and depth if your engine can; the quality depends heavily on them. And treat it, again, as a net rather than a plan.
CSCE 650 · Virtual Reality — Module 06
10

## Slide 12
REDUCING
What actually reduces latency
▪ Hit the frame budget. Everything else is secondary; a missed frame costs a whole refresh period.
▪ Late latching: read the pose as late as possible in the frame (Module 05).
▪ Shorten the CPU-GPU pipeline. Deep buffering adds a frame of latency per stage; VR wants a shallow pipeline even at some throughput cost.
▪ Avoid temporal effects that need several frames of history — they add perceived latency even when the timing is correct.
▪ Higher refresh rate reduces scan-out latency directly.
The deep-pipeline point is the one that surprises people porting from flat-screen engines.
CSCE 650 · Virtual Reality — Module 06
11

## Slide 13
Measure latency; do not estimate it
HOW TO ACTUALLY KNOW
The pendulum method: swing a tracked controller in front of a camera that sees both the controller and the display, and count frames between the two.
A photodiode on the display plus an instrumented input gives a precise electrical measurement.
Some runtimes report it — use it, and verify it against a physical measurement at least once.
Estimating from frame time is wrong, because it omits scan-out, pixel response, and the compositor. The usual estimate is roughly half the true figure.
CSCE 650 · Virtual Reality — Module 06
12

## Slide 14
What to carry forward
1. Motion-to-photon latency has seven stages and the application controls roughly half of them. The target is under 20 ms total.
2. Below ~20 ms the world feels attached to the room; above it, attached to the head. The symptom is discomfort, not a perception of lag.
3. Timewarp reprojects the finished frame to a newer pose. For rotation it is nearly exact, because no information is missing.
4. For translation it is not, because parallax changes reveal geometry that was never rendered — which is why translation latency matters more.
5. Asynchronous timewarp keeps the world stable through a missed frame; it is a safety net, and relying on it halves your animation rate.
6. Measure latency physically. Estimating it from frame time omits scan-out, pixel response, and the compositor, and understates it by about half.
CSCE 650 · Virtual Reality — Module 06
13