## Slide 1
UNIVERSITY OF CLAUDE
CSCE 650 — Virtual Reality
MODULE 10
Rendering for VR
Twice the pixels, half the time.
CSCE 650 · Module 10 of 13 · original material, share freely

## Slide 2
MODULE OUTCOMES
What you will be able to do
▪ Apply stereo rendering optimisations and say what each saves.
▪ Explain foveated rendering, fixed and eye-tracked.
▪ Explain variable rate shading and where to apply it.
▪ Choose antialiasing appropriately for VR.
▪ Build a VR performance budget and defend it.
CSCE 650 · Virtual Reality — Module 10
1
Notes: State the outcomes before the content. Every slide that follows exists to serve one of these.

## Slide 3
PART 1
Two eyes, cheaply
Exploiting what the eyes share.
CSCE 650 · Virtual Reality — Module 10
2

## Slide 4
STEREO
Stereo rendering techniques
Technique
How
Saves
Sequential
Render twice, independently
Nothing — the baseline
Instanced stereo
One draw call, instanced per eye
CPU draw calls; ~40% CPU
Multiview
GPU renders both views from one submission
CPU and vertex work
Single-pass
Both eyes in one wide render target
Setup and state changes
CSCE 650 · Virtual Reality — Module 10
3
Notes: The 'fragment work cannot be shared' point bounds how much these techniques can possibly save.

## Slide 5
What can and cannot be shared
THE LIMIT ON STEREO OPTIMISATION
Fully shareable: shadow map generation, lightmaps, culling (mostly), animation and skinning, physics, and all CPU simulation.
Partly shareable: vertex processing — multiview transforms once and projects twice.
Not shareable: fragment shading. The two eyes see different pixels, and that difference is stereo.
So the ceiling is bounded by your fragment cost. A vertex-bound scene benefits enormously from multiview; a fragment-bound one barely at all — and most VR scenes are fragment-bound.
CSCE 650 · Virtual Reality — Module 10
4

## Slide 6
PART 2
Foveated rendering
Spending pixels where the eye can use them.
CSCE 650 · Virtual Reality — Module 10
5

## Slide 7
TWO KINDS
Fixed and eye-tracked
Fixed foveated
▪ Assume the user looks mostly forward.
▪ Reduce shading rate toward the edges.
▪ No eye tracking required.
  – Conservative — the fovea could be anywhere.
▪ Typical saving 20–40%.
Eye-tracked foveated
▪ Follow the actual gaze.
▪ Full rate only at the real fovea.
▪ Needs eye tracking with low latency.
  – Aggressive — the fovea is known.
▪ Typical saving 50–70%.
CSCE 650 · Virtual Reality — Module 10
6
Notes: The latency requirement for eye-tracked foveation is strict — saccades are fast and a late update is visible.

## Slide 8
Foveated rendering must beat the saccade
THE HARD REQUIREMENT
A saccade takes 20–50 ms and can cover 20°. If the foveal region updates after the eye arrives, the user sees low-resolution content at the centre of vision.
Which is immediately obvious — far more noticeable than uniformly lower resolution would be.
So the eye tracker's latency plus the rendering latency must fit inside the saccade, which is demanding.
Saccadic suppression helps — vision is substantially suppressed during a saccade, which buys some of the time back and is actively exploited.
CSCE 650 · Virtual Reality — Module 10
7

## Slide 9
VRS
Variable rate shading
▪ Shade one value per 2×2 or 4×4 block of pixels instead of per pixel, where detail is not needed.
▪ Hardware support makes it nearly free — it is a rasteriser feature, not a post-process.
▪ Drive it by eccentricity (foveation), by motion, or by material — a flat wall needs less shading rate than a detailed surface.
▪ Geometry and depth remain full rate, so edges stay sharp — which is why the artefacts are subtle.
▪ It composes with everything else, which makes it unusually easy to adopt.
CSCE 650 · Virtual Reality — Module 10
8
Notes: VRS is the most practical of these techniques because the hardware does it and edges stay sharp.

## Slide 10
PART 3
Choices that differ from flat rendering
Where VR inverts the usual advice.
CSCE 650 · Virtual Reality — Module 10
9

## Slide 11
REVERSALS
VR-specific rendering decisions
Usual practice
In VR
TAA is the default antialiasing
MSAA often wins — TAA smears under constant head motion
Deferred rendering for many lights
Forward+ often wins — MSAA, bandwidth, transparency
Motion blur adds realism
Never use it (Module 02)
Post-processing is cheap
Doubled, and bandwidth-bound
Dynamic resolution on demand
Essential, and must be smooth
CSCE 650 · Virtual Reality — Module 10
10
Notes: The deferred/forward reversal is the one with the biggest architectural consequences.

## Slide 12
Why forward rendering came back for VR
THE ARCHITECTURAL REVERSAL
MSAA works with forward rendering and not with deferred — and VR wants MSAA (Module 02).
Deferred's G-buffer bandwidth is doubled by stereo, and VR is frequently bandwidth-bound rather than shading-bound.
Transparency is awkward in deferred, and VR content tends to have a lot of it.
Forward+ or clustered forward gets many lights without the G-buffer, which is why several VR-focused renderers moved back. This is a genuine architectural decision, not a tuning one.
CSCE 650 · Virtual Reality — Module 10
11

## Slide 13
Dynamic resolution is not optional
THE PRACTICAL NECESSITY
Content is not uniform. Some views are cheap and some are expensive, and the user controls which they are looking at.
Fixed resolution means either wasting headroom or missing frames, and missing frames is the one thing you cannot do (Module 01).
So scale the render target per frame to hit the budget, and let quality vary instead of frame time.
Change it smoothly. A sudden resolution change is visible as a pop; ramping over several frames is not. This is the detail implementations get wrong.
CSCE 650 · Virtual Reality — Module 10
12

## Slide 14
BUDGET
Building a VR performance budget
▪ Start from the frame budget — 11.1 ms at 90 Hz — and subtract the compositor's share.
▪ Allocate explicitly: so much for shadows, so much for opaque, so much for transparency, so much for post.
▪ Leave 20% headroom. The expensive view exists, and the user will find it.
▪ Measure per eye and in the worst case, not the average view.
▪ Profile on the target hardware. Standalone headsets are mobile GPUs with mobile thermal limits, and they throttle.
Thermal throttling on standalone hardware means a scene that passes for two minutes may fail after ten.
CSCE 650 · Virtual Reality — Module 10
13

## Slide 15
What to carry forward
1. Instanced stereo and multiview share setup and vertex work; fragment work can never be shared, which bounds what they can save.
2. Fixed foveated rendering assumes a forward gaze and saves 20–40%; eye-tracked foveation knows the gaze and saves 50–70%.
3. Eye-tracked foveation must update faster than a saccade completes, or the user sees low resolution at the centre of vision.
4. Variable rate shading reduces shading rate per block while keeping geometry and depth at full rate, so the artefacts stay subtle.
5. VR reverses several defaults: MSAA over TAA, forward over deferred, and never motion blur.
6. Dynamic resolution is necessary because the user chooses the view; ramp it smoothly or the change is visible.
CSCE 650 · Virtual Reality — Module 10
14