## Slide 1
UNIVERSITY OF CLAUDE
CSCE 735 — Parallel Computing
MODULE 08
GPU Programming
Thousands of threads, and a machine that only makes sense once.
CSCE 735 · Module 08 of 13 · original material, share freely

## Slide 2
MODULE OUTCOMES
What you will be able to do
▪ Explain the CUDA execution model and map it to the hardware.
▪ Explain warps and why divergence costs.
▪ Explain the memory hierarchy and coalescing.
▪ Explain occupancy and what it is for.
▪ Write a correct kernel and launch it.
CSCE 735 · Parallel Computing — Module 08
1
Notes: State the outcomes before the content. Every slide that follows exists to serve one of these.

## Slide 3
PART 1
The execution model
Threads, blocks, and grids.
CSCE 735 · Parallel Computing — Module 08
2

## Slide 4
CUDA
The model, and the hardware under it
text
SOFTWARE HARDWARE
-------- --------
thread --> one lane
WARP (32 threads) --> executed in LOCKSTEP, always
block (up to 1024) --> resident on ONE streaming multiprocessor
(shares that SM's shared memory)
grid (many blocks) --> distributed across all SMs
KEY FACTS:
* A warp is the real unit of execution. Blocks are divided into
warps and warps are scheduled; individual threads are not.
* Threads in a block can synchronise (__syncthreads) and share
memory. Threads in different blocks CANNOT, except via global
memory and a kernel boundary.
* Blocks must be independent -- they may run in any order, and
any subset may run concurrently. This is what makes the model
scale across devices with different SM counts.
Blocks being independent is what lets the same binary run on a device with 4 SMs and one with 128.
CSCE 735 · Parallel Computing — Module 08
3
Notes: Block independence is the design decision that makes CUDA portable across a decade of hardware.

## Slide 5
The warp is the real unit, not the thread
THE FACT THAT EXPLAINS THE REST
32 threads execute in lockstep, issuing the same instruction each cycle. The hardware schedules warps, not threads.
So a block of 100 threads occupies four warps, the last of which is 28/32 idle. Always use multiples of 32.
And a branch that goes different ways within a warp serialises — both paths execute, with the inactive lanes masked off.
Everything about GPU performance follows from this. Divergence, coalescing, and occupancy are all consequences of lockstep execution.
CSCE 735 · Parallel Computing — Module 08
4

## Slide 6
Divergence: both branches execute
THE COST
If some lanes in a warp take the if and others the else, the warp executes both, masking the inactive lanes each time.
So the cost is the sum of the branches, not the maximum. A two-way branch costs twice.
Divergence between warps is free. Warp 0 taking one path and warp 1 another costs nothing — they are scheduled independently.
So organise data so that threads in the same warp take the same path — sort by branch condition, or pad, or restructure. This is frequently a large win.
CSCE 735 · Parallel Computing — Module 08
5

## Slide 7
PART 2
Memory
Where GPU performance is actually won.
CSCE 735 · Parallel Computing — Module 08
6

## Slide 8
HIERARCHY
The GPU memory hierarchy
Space
Scope
Latency
Note
Registers
One thread
~1 cycle
Plentiful; limits occupancy
Shared
One block
~20 cycles
Programmer-managed cache
L1 / L2
SM / device
~30/200
Automatic
Global
Device
~400–800
Large, slow, coalescing matters
Constant
Device, read-only
Cached
Broadcast to a whole warp cheaply
Local
One thread
Global speed
Register spills. Avoid
CSCE 735 · Parallel Computing — Module 08
7
Notes: 'Local' memory being global-speed surprises people and spilling is a common silent performance bug.

## Slide 9
Coalescing: the warp's accesses must be contiguous
THE SINGLE MOST IMPORTANT MEMORY RULE
The memory system serves a warp's 32 accesses as a small number of wide transactions.
If the 32 threads read 32 consecutive floats, that is one 128-byte transaction. Perfect.
If they read 32 scattered addresses, that is up to 32 separate transactions — 32× the memory traffic for the same data.
So thread i should access element i, and arrays should be structure-of-arrays. The same rule as Module 02, with a much steeper penalty.
CSCE 735 · Parallel Computing — Module 08
8

## Slide 10
COALESCING
The pattern that matters
cpp
// COALESCED: consecutive threads read consecutive addresses.
__global__ void good(float* a, float* b, float* c, int n) {
int i = blockIdx.x * blockDim.x + threadIdx.x;
if (i < n) c[i] = a[i] + b[i]; // thread i -> element i
}
// NOT COALESCED: stride between consecutive threads.
__global__ void bad(float* a, float* c, int n, int stride) {
int i = blockIdx.x * blockDim.x + threadIdx.x;
if (i*stride < n) c[i] = a[i * stride]; // scattered
}
// NOT COALESCED: array of structures -- each thread wants one
// field, so the warp reads 32 widely separated words.
struct P { float x, y, z, w; };
__global__ void aos(P* p, float* out, int n) {
int i = ...; out[i] = p[i].x; // reads 1 of every 4 floats
}
// FIX: separate arrays for x, y, z, w (structure of arrays).
The array-of-structures case is the one that appears in real code and silently costs 4×.
CSCE 735 · Parallel Computing — Module 08
9
Notes: The AoS case is worth running — the measured difference is convincing in a way the explanation is not.

## Slide 11
PART 3
Occupancy
Having enough threads to hide latency.
CSCE 735 · Parallel Computing — Module 08
10

## Slide 12
Occupancy exists to hide memory latency
WHAT IT IS FOR
Global memory latency is 400 to 800 cycles. A CPU hides this with caches and prediction; a GPU hides it by switching to another warp.
Occupancy is the fraction of the maximum resident warps that are actually resident.
More resident warps means more candidates to switch to, so more latency is covered.
It is limited by registers per thread, shared memory per block, and block size. Using too many registers reduces the warps that fit — which is a real tuning trade-off.
CSCE 735 · Parallel Computing — Module 08
11

## Slide 13
Maximum occupancy is not the goal
THE COMMON MISUNDERSTANDING
Occupancy is a means, not an end. The goal is to saturate the limiting resource — usually memory bandwidth.
A kernel at 50% occupancy that saturates bandwidth is finished. Raising occupancy achieves nothing.
And more registers per thread can beat more warps, because instruction-level parallelism within a thread also hides latency.
Volkov's result: several kernels run faster at lower occupancy with more work per thread. Measure, do not maximise the metric.
CSCE 735 · Parallel Computing — Module 08
12

## Slide 14
PRACTICE
Getting a kernel working
▪ Check every error. Kernel launches fail asynchronously; without checking you see a wrong answer, not an error.
▪ Use compute-sanitizer — the CUDA memcheck and race detector. Catches out-of-bounds and races.
▪ Verify against the CPU result before optimising anything.
▪ Guard the bounds. Grid size rounds up, so some threads are past the end. if (i < n) is not optional.
▪ And profile with Nsight Compute, which reports the limiting resource directly.
Asynchronous launch failure is the one that costs beginners the most time — the error surfaces at the next synchronisation, far from its cause.
CSCE 735 · Parallel Computing — Module 08
13

## Slide 15
What to carry forward
1. A warp of 32 threads executes in lockstep and is the real unit of scheduling — everything about GPU performance follows from that.
2. Blocks must be independent, which is what lets one binary scale across devices with very different SM counts.
3. A divergent branch within a warp executes both paths with masking, so the cost is the sum; divergence between warps is free.
4. Coalescing is the most important memory rule: thread i should access element i, or the warp costs up to 32 transactions instead of one.
5. Occupancy exists to hide memory latency by providing warps to switch to, and is limited by registers and shared memory.
6. Maximum occupancy is not the goal — several kernels run faster at lower occupancy with more work per thread.
CSCE 735 · Parallel Computing — Module 08
14