## Slide 1
UNIVERSITY OF CLAUDE
CSCE 748 — Computational Photography
MODULE 01
What a Camera Measures
The measurement, and everything that is not in it.
CSCE 748 · Module 01 of 13 · original material, share freely

## Slide 2
MODULE OUTCOMES
What you will be able to do
▪ Describe image formation from scene radiance to stored value.
▪ Explain the exposure triangle in terms of what each control does to the measurement.
▪ Explain what a raw file contains and what it does not.
▪ Explain noise sources and why they behave as they do.
▪ Explain why linearity matters and where it is lost.
CSCE 748 · Computational Photography — Module 01
1
Notes: State the outcomes before the content. Every slide that follows exists to serve one of these.

## Slide 3
PART 1
Formation
From the scene to a number.
CSCE 748 · Computational Photography — Module 01
2

## Slide 4
PIPELINE
Scene radiance to stored value
text
scene radiance L(x, y, lambda) [W / m^2 / sr]
| lens: aperture, focal length, vignetting, aberration
v
image irradiance E(x, y, lambda) [W / m^2]
| shutter: integrate over exposure time t
v
photon count per sensor well [electrons]
| colour filter array: one channel per pixel
| quantum efficiency, full well capacity
v
analogue voltage
| analogue gain (ISO)
v
ADC --> RAW INTEGER [12-14 bits, LINEAR]
| demosaic, white balance, colour matrix, tone curve
v
display image [8 bits, NON-LINEAR]
*** The raw integer is proportional to photon count. ***
*** Everything after the ADC is interpretation. ***
The raw value is a measurement. Everything below the ADC line is a series of choices, and this course is about those choices.
CSCE 748 · Computational Photography — Module 01
3
Notes: The measurement/interpretation boundary is the spine of the whole course. Place it carefully.

## Slide 5
EXPOSURE
What each control actually does
Control
Changes
Side effect
Aperture
Light gathered per unit time
Depth of field; diffraction when small
Shutter
Integration time
Motion blur
ISO
Gain, not light
Amplifies signal AND noise
CSCE 748 · Computational Photography — Module 01
4
Notes: The ISO misconception is near-universal and worth correcting explicitly.

## Slide 6
Only two controls change how many photons you collect
THE CONSEQUENCE
Aperture and shutter time determine the photon count. ISO does not.
Photon count determines the noise floor (Part 3), so image quality is set by those two alone.
ISO is a decision about where to put the measurement in the ADC's range — useful, and not a way to get more signal.
This is why 'expose to the right' works: collect as many photons as the highlights permit, because you cannot add them afterwards.
CSCE 748 · Computational Photography — Module 01
5

## Slide 7
PART 2
The raw file
What is in it, and what is not.
CSCE 748 · Computational Photography — Module 01
6

## Slide 8
CONTENTS
Raw and JPEG
Raw contains
▪ Linear sensor values, 12–14 bits.
▪ One colour per pixel (the CFA pattern).
▪ No white balance applied — only recorded as metadata.
  – Black level, saturation point, colour matrix.
▪ The measurement.
JPEG contains
▪ Non-linear, 8 bits, gamma encoded.
▪ Three colours per pixel, demosaiced.
▪ White balance baked in, irreversibly.
  – Tone curve, sharpening, noise reduction applied.
▪ An interpretation.
CSCE 748 · Computational Photography — Module 01
7
Notes: The irreversibility of the JPEG decisions is the practical argument for shooting raw.

## Slide 9
Linearity is the property that makes everything work
WHY IT MATTERS SO MUCH
A raw value of 2000 corresponds to twice the light of 1000. Exactly.
So you can add, average, and scale radiance meaningfully — which is what HDR merging (Module 03), burst averaging (Module 10), and every physically-based operation require.
A gamma-encoded JPEG value does not have this property. Averaging two gamma-encoded pixels gives the wrong answer, and the error is not small.
So: do all processing in linear space and encode at the very end — exactly the rule CSCE 647 Module 13 arrived at from the rendering side.
CSCE 748 · Computational Photography — Module 01
8

## Slide 10
PART 3
Noise
Where it comes from and how it scales.
CSCE 748 · Computational Photography — Module 01
9

## Slide 11
NOISE
The sources, and which dominates
shot noise: σ = √N
Photon arrival is Poisson. The noise is the square root of the count — a property of light, not of the sensor.
SNR = N / √N = √N
So signal-to-noise improves as the square root of photon count. Four times the light, twice the SNR.
read noise: constant; dark current: ∝ time, temperature
Sensor-dependent, and dominant only in very dim conditions or long exposures.
Shot noise dominates in normal conditions and cannot be engineered away — it is in the light itself.
CSCE 748 · Computational Photography — Module 01
10
Notes: That shot noise is a property of light rather than of the sensor surprises people and explains a lot.

## Slide 12
Shot noise is why low light is hard
THE FUNDAMENTAL LIMIT
Photons arrive as a Poisson process. Count N on average, and the standard deviation is √N.
In bright light N is large — 10,000 photons gives an SNR of 100, and the noise is invisible.
In dim light N is small — 100 photons gives an SNR of 10, and the noise is the image.
No sensor improvement fixes this, because the noise is in the light. The only remedy is collecting more photons — a larger aperture, a longer exposure, or more frames, which is Module 10's entire premise.
CSCE 748 · Computational Photography — Module 01
11

## Slide 13
CONSEQUENCES
What follows for the rest of the course
▪ Averaging n frames improves SNR by √n — because the signal adds and the noise adds in quadrature. Module 10.
▪ Denoising is estimation under a known noise model, not guesswork. Knowing the noise is Poisson-Gaussian is what makes it tractable.
▪ Noise is signal-dependent, so it is stronger in the highlights and more visible in the shadows.
▪ Which means denoising must be applied in linear space, before the tone curve changes the relationship.
Applying denoising after gamma encoding is a common mistake and produces visibly worse results.
CSCE 748 · Computational Photography — Module 01
12

## Slide 14
What to carry forward
1. A raw value is proportional to photon count. Everything after the ADC — demosaic, white balance, tone curve — is interpretation.
2. Aperture and shutter change how many photons you collect; ISO is gain and amplifies signal and noise alike.
3. Raw is linear, single-channel-per-pixel, and keeps white balance as metadata; JPEG is encoded, demosaiced, and has every decision baked in.
4. Linearity is what makes averaging and merging meaningful, which is why all processing happens in linear space and encoding happens last.
5. Shot noise is √N because photon arrival is Poisson — it is a property of light, not of the sensor, and cannot be engineered away.
6. SNR improves as √N, so averaging n frames gains √n — which is the entire premise of burst photography.
CSCE 748 · Computational Photography — Module 01
13