## Slide 1
UNIVERSITY OF CLAUDE
CSCE 748 — Computational Photography
MODULE 05
Demosaicing and the Raw Pipeline
Two-thirds of the colour data was never measured.
CSCE 748 · Module 05 of 13 · original material, share freely

## Slide 2
MODULE OUTCOMES
What you will be able to do
▪ Explain the colour filter array and why it exists.
▪ Implement demosaicing and explain its failure modes.
▪ Explain white balance and the illuminant estimation problem.
▪ Trace the full raw-to-display pipeline and justify the ordering.
▪ Explain colour spaces and the camera colour matrix.
CSCE 748 · Computational Photography — Module 05
1
Notes: State the outcomes before the content. Every slide that follows exists to serve one of these.

## Slide 3
PART 1
The colour filter array
One colour per pixel, interpolated into three.
CSCE 748 · Computational Photography — Module 05
2

## Slide 4
A sensor measures intensity, not colour
WHY THE MOSAIC EXISTS
A photosite counts photons. It has no way to distinguish their wavelengths.
So each pixel gets a colour filter — the Bayer pattern is 50% green, 25% red, 25% blue, arranged in 2×2 tiles.
Twice as many green because luminance sensitivity peaks there and the eye resolves detail largely from the green channel.
So two-thirds of the colour data at every pixel is interpolated, not measured. Demosaicing is the reconstruction, and its errors are visible as colour artefacts.
CSCE 748 · Computational Photography — Module 05
3

## Slide 5
DEMOSAIC
Demosaicing methods
Method
Idea
Quality
Nearest neighbour
Copy the nearest same-colour pixel
Bad; blocky
Bilinear
Average the neighbours of each colour
Soft; colour fringes at edges
Edge-directed
Interpolate along edges, not across
Much better
Gradient-corrected
Use the green channel's detail to guide R and B
The classic good method
Learned
A network trained on raw/RGB pairs
Best, and it invents
CSCE 748 · Computational Photography — Module 05
4
Notes: The green-as-guide insight is what separates good demosaicing from bilinear.

## Slide 6
Demosaicing errors are structural, not random
THE CHARACTERISTIC ARTEFACTS
Zippering: alternating colour along a horizontal or vertical edge, from interpolating across it.
Colour moiré: fine repeating detail near the sampling limit aliases differently in each channel, producing coloured bands where the scene is grey.
False colour at sharp edges and on fine texture.
These are aliasing artefacts (Module 02), which is why optical low-pass filters exist — and why removing them trades sharpness for exactly these.
CSCE 748 · Computational Photography — Module 05
5

## Slide 7
PART 2
White balance
Deciding what colour the light was.
CSCE 748 · Computational Photography — Module 05
6

## Slide 8
Colour constancy is an inference, and it is underdetermined
THE PROBLEM
The sensor measures reflected light — the product of illumination and surface reflectance.
Separating them is underdetermined. A white surface under orange light and an orange surface under white light produce identical measurements.
Humans do it anyway, remarkably well, using scene context, memory of object colours, and the range of colours present.
Cameras estimate it with heuristics, and get it wrong in exactly the cases where the assumptions fail.
CSCE 748 · Computational Photography — Module 05
7

## Slide 9
ESTIMATION
Illuminant estimation heuristics
Method
Assumption
Fails when
Grey world
The scene averages to grey
A large uniform colour dominates
White patch
The brightest pixel is white
No white object; a clipped highlight
Grey edge
Average of edges is achromatic
More robust than grey world
Gamut mapping
Observed gamut constrains the illuminant
Few colours present
Learned
Trained on labelled images
Scenes unlike the training set
CSCE 748 · Computational Photography — Module 05
8
Notes: Having a counterexample for each heuristic makes the underdetermination concrete.

## Slide 10
PART 3
The pipeline
Order matters, and the reasons are specific.
CSCE 748 · Computational Photography — Module 05
9

## Slide 11
PIPELINE
Raw to display, in order
text
1. SUBTRACT BLACK LEVEL sensor's zero is not 0
2. SCALE to [0,1] using the saturation value
3. WHITE BALANCE per-channel multipliers
(BEFORE demosaic: channels become comparable)
4. DEMOSAIC one channel -> three
5. COLOUR MATRIX camera RGB -> XYZ -> working space
6. DENOISE / SHARPEN IN LINEAR SPACE (Module 01)
7. TONE MAP HDR -> display range (Module 04)
8. GAMUT MAP handle out-of-gamut colours
9. ENCODE apply the display transfer function
<-- LAST. ONCE.
Steps 1-6 are LINEAR. Step 9 is where linearity ends.
White balance before demosaicing because the interpolation assumes the channels are comparable — which they are not until it is applied.
CSCE 748 · Computational Photography — Module 05
10
Notes: The white-balance-before-demosaic ordering is the non-obvious one and students get it wrong.

## Slide 12
Why white balance comes before demosaicing
THE ORDERING THAT SURPRISES PEOPLE
Demosaicing interpolates between channels — the good methods use the green channel to guide red and blue.
That assumes the channels are on comparable scales. Before white balance they are not: under tungsten light the blue channel may be a quarter of the red.
So interpolation guided by an uncorrected green channel introduces colour errors at exactly the edges where demosaicing is already hardest.
Apply the per-channel multipliers first, and the channels become comparable before the interpolation needs them to be.
CSCE 748 · Computational Photography — Module 05
11

## Slide 13
COLOUR
Colour spaces, briefly
▪ Camera RGB is device-specific — it depends on the filters' spectral responses and means nothing outside that camera.
▪ The colour matrix maps it to XYZ, a device-independent space defined by the CIE standard observer.
▪ Then XYZ to a working space — sRGB, Adobe RGB, ProPhoto, ACEScg. Wider spaces preserve saturated colours and need more bits.
▪ The mapping is approximate, because camera filters do not match the human cone responses — no 3×3 matrix is exact.
▪ This is why two cameras render the same scene differently, even with identical white balance.
CSCE 748 · Computational Photography — Module 05
12
Notes: The 'no 3x3 matrix is exact' point explains camera colour differences better than any amount of brand folklore.

## Slide 14
What to carry forward
1. A photosite counts photons and cannot distinguish wavelength, so a colour filter array samples one channel per pixel — two-thirds of the colour data is interpolated.
2. The Bayer pattern is half green because luminance detail is carried largely by green, and good demosaicing uses green to guide red and blue.
3. Zippering, colour moiré, and false colour are aliasing artefacts, which is why optical low-pass filters exist.
4. White balance is an underdetermined inference — a white surface under orange light is indistinguishable from an orange surface under white light.
5. Every illuminant heuristic has a scene that defeats it: grey world fails on a forest, white patch fails on snow.
6. White balance comes before demosaicing because interpolation assumes the channels are on comparable scales, and before correction they are not.
CSCE 748 · Computational Photography — Module 05
13