## Slide 1
UNIVERSITY OF CLAUDE
CSCE 748 — Computational Photography
MODULE 06
Deconvolution and Deblurring
Undoing a blur, and why it is mostly impossible.
CSCE 748 · Module 06 of 13 · original material, share freely

## Slide 2
MODULE OUTCOMES
What you will be able to do
▪ Model blur as convolution with a point spread function.
▪ Explain why naive inverse filtering fails.
▪ Implement Wiener and Richardson–Lucy deconvolution.
▪ Explain blind deconvolution and why it is ill-posed.
▪ Explain coded apertures and flutter shutters.
CSCE 748 · Computational Photography — Module 06
1
Notes: State the outcomes before the content. Every slide that follows exists to serve one of these.

## Slide 3
PART 1
Blur as convolution
The forward model.
CSCE 748 · Computational Photography — Module 06
2

## Slide 4
MODEL
The blur model
b = k * s + n
Blurred image = kernel convolved with sharp image, plus noise. The kernel is the point spread function.
B = K · S + N
In the frequency domain, convolution becomes multiplication — which is why deconvolution is attempted there.
S = (B − N) / K ← the naive inverse
Divide by the kernel's spectrum. And this is catastrophic, for the reason on the next slide.
The forward model is simple and exact. The inverse is where the difficulty is.
CSCE 748 · Computational Photography — Module 06
3
Notes: Setting up the forward model cleanly makes the inverse problem's difficulty obvious.

## Slide 5
Naive inverse filtering amplifies noise without bound
WHY YOU CANNOT JUST DIVIDE
A blur is a low-pass filter, so K is near zero at high frequencies.
Dividing by a near-zero number amplifies whatever is there — and what is there, at those frequencies, is almost entirely noise.
So the 'recovered' image is dominated by amplified noise, usually by a wide margin, and looks far worse than the blurred input.
And where K is exactly zero, the information is genuinely gone. No algorithm recovers it, because nothing was recorded. This is the fundamental limit.
CSCE 748 · Computational Photography — Module 06
4

## Slide 6
PART 2
Regularised deconvolution
Trading sharpness against noise.
CSCE 748 · Computational Photography — Module 06
5

## Slide 7
WIENER
Wiener deconvolution
S = B · K* / ( |K|² + 1/SNR )
Divide by K, but add a term that prevents the division blowing up where K is small.
where SNR is large: → 1/K (full inversion)
Where the signal is strong, invert normally.
where SNR is small: → K* · SNR (suppress)
Where the noise dominates, suppress rather than amplify.
An optimal linear filter under a Gaussian noise assumption. One parameter, and it is the noise level.
CSCE 748 · Computational Photography — Module 06
6
Notes: The frequency-by-frequency behaviour is the intuition: trust the measurement where it is reliable.

## Slide 8
Richardson–Lucy: iterate toward the answer
THE NON-LINEAR ALTERNATIVE
An iterative maximum-likelihood method assuming Poisson noise — which is the correct model for photon counting (Module 01).
Each iteration compares the current estimate's blur against the observation and corrects multiplicatively.
It preserves non-negativity automatically, which is physically correct and which Wiener does not.
And it amplifies noise as iterations increase, so you must stop early. The stopping point is a tuning parameter disguised as a convergence criterion, which is worth being honest about.
CSCE 748 · Computational Photography — Module 06
7

## Slide 9
PRIORS
Regularisation by image priors
Prior
Assumes
Effect
Tikhonov (L2)
The image is smooth
Blurs edges — wrong prior
Total variation
Piecewise constant
Preserves edges; flattens texture
Sparse gradients
Natural images have few strong edges
Matches real statistics well
Learned
Whatever the training data showed
Best results; invents detail
CSCE 748 · Computational Photography — Module 06
8
Notes: The sparse-gradient prior is the one with genuine empirical support and it transformed the field around 2006.

## Slide 10
PART 3
Blind deconvolution
When you do not know the blur either.
CSCE 748 · Computational Photography — Module 06
9

## Slide 11
Blind deconvolution is severely ill-posed
WHY IT IS HARD
You observe b and must recover both k and s. There are far more unknowns than measurements.
And there is a trivial wrong answer: k = delta function, s = b. Sharp kernel, blurred image, perfect agreement with the observation.
So the problem is entirely driven by the priors. What makes a plausible image, and what makes a plausible blur kernel?
Fergus et al. 2006 was the breakthrough — use the heavy-tailed gradient statistics of natural images as the prior, and the delta solution becomes unlikely.
CSCE 748 · Computational Photography — Module 06
10

## Slide 12
PRACTICE
What makes blind deblurring work
▪ Natural image priors — sparse gradients, as above. The core idea.
▪ Kernel priors: motion blur kernels are sparse, connected, and non-negative. A camera shake path is a curve, not a cloud.
▪ Coarse-to-fine (Module 02): estimate a small kernel at low resolution, refine.
▪ Edge prediction: guess where the strong edges should be, and use them to constrain the kernel.
▪ Or measure the blur — an IMU records the camera shake directly, which is far easier than inferring it.
CSCE 748 · Computational Photography — Module 06
11
Notes: The IMU point is the practical one: measurement beats inference when it is available.

## Slide 13
PART 4
Coded imaging
Change the capture so the inverse is easier.
CSCE 748 · Computational Photography — Module 06
12

## Slide 14
CODED CAPTURE
Two ways to make deconvolution tractable
Coded aperture
▪ Put a patterned mask in the aperture.
▪ The defocus PSF becomes broadband — no zeros in its spectrum.
▪ So deconvolution is well-conditioned.
  – And the PSF's scale reveals depth.
▪ Cost: light is blocked by the mask.
Flutter shutter
▪ Open and close the shutter in a coded sequence during exposure.
▪ The motion blur PSF becomes broadband instead of a box.
▪ A box kernel has zeros; a coded one does not.
  – Motion blur becomes invertible.
▪ Cost: half the light, and you must know the motion.
CSCE 748 · Computational Photography — Module 06
13
Notes: Both are the same idea: engineer the PSF so its spectrum has no zeros, because zeros are unrecoverable.

## Slide 15
The deep idea: design the measurement, not just the algorithm
WHAT COMPUTATIONAL PHOTOGRAPHY MEANS
A conventional camera is designed to form an image directly. If the image is blurred, you are stuck with an ill-posed inverse.
A coded camera is designed so that the inverse is easy — accepting a worse raw image in exchange for a better recoverable one.
This is the central move of the whole field: co-design the optics and the computation rather than treating the camera as fixed.
Light field cameras (Module 09) are the same move, as is burst photography (Module 10) — capture something that is not a photograph, and compute the photograph from it.
CSCE 748 · Computational Photography — Module 06
14

## Slide 16
What to carry forward
1. Blur is convolution with a point spread function, so deconvolution is division in the frequency domain — and that division is catastrophic.
2. A blur is low-pass, so its spectrum is near zero at high frequencies; dividing amplifies the noise that lives there.
3. Where the spectrum is exactly zero the information is genuinely gone, and no algorithm recovers it.
4. Wiener deconvolution adds a noise term so the division suppresses rather than amplifies where the signal is weak.
5. Richardson–Lucy assumes Poisson noise and preserves non-negativity, and must be stopped early — which is a tuning parameter disguised as convergence.
6. Coded apertures and flutter shutters engineer the PSF to have no spectral zeros: design the measurement so the inverse is easy.
CSCE 748 · Computational Photography — Module 06
15