## Slide 1
UNIVERSITY OF CLAUDE
CSCE 748 — Computational Photography
MODULE 09
Light Fields and Plenoptic Cameras
Capturing rays instead of pixels.
CSCE 748 · Module 09 of 13 · original material, share freely

## Slide 2
MODULE OUTCOMES
What you will be able to do
▪ Define the plenoptic function and the 4D light field.
▪ Explain how a plenoptic camera trades resolution for angle.
▪ Explain digital refocusing and synthetic aperture.
▪ Explain why light field cameras failed commercially.
▪ Identify where light fields are actually used.
CSCE 748 · Computational Photography — Module 09
1
Notes: State the outcomes before the content. Every slide that follows exists to serve one of these.

## Slide 3
PART 1
The plenoptic function
Everything that could be seen.
CSCE 748 · Computational Photography — Module 09
2

## Slide 4
PLENOPTIC
From seven dimensions to four
P(x, y, z, θ, φ, λ, t)
The full plenoptic function: radiance at every position, in every direction, at every wavelength and time. Seven dimensions.
L(u, v, s, t)
Fix time and wavelength, and assume free space, where radiance is constant along a ray (CSCE 647 Module 01). A ray is then determined by where it crosses two planes.
Radiance invariance reduces five spatial dimensions to four. The same fact that made ray tracing a lookup makes light fields finite.
CSCE 748 · Computational Photography — Module 09
3
Notes: The connection to CSCE 647 Module 01 is exact and worth drawing — the same invariance, used in reverse.

## Slide 5
A photograph is a 2D slice of a 4D function
THE REFRAMING
A conventional camera integrates over the aperture, collapsing all the rays arriving at a sensor point into one value.
That integration is irreversible — the angular information is destroyed at capture.
A light field camera records the rays separately, keeping which direction each one came from.
So the integration can be performed afterwards, differently — a different aperture, a different focus, a different viewpoint. Capture the function; compute the photograph.
CSCE 748 · Computational Photography — Module 09
4

## Slide 6
PART 2
Capture
Three ways to sample four dimensions.
CSCE 748 · Computational Photography — Module 09
5

## Slide 7
CAPTURE
How to record a light field
Method
How
Trade
Camera array
Many cameras on a grid
Full resolution; bulky, expensive
Gantry
One camera moved mechanically
Static scenes only
Plenoptic (microlens)
A microlens array over the sensor
One shot; resolution falls hard
Coded mask
A patterned mask near the sensor
Compressive; needs reconstruction
CSCE 748 · Computational Photography — Module 09
6
Notes: The severity of the resolution trade is the commercial story in Part 4.

## Slide 8
The resolution trade is brutal
THE ARITHMETIC THAT DECIDED THE MARKET
A microlens array places a small lens over each group of sensor pixels. The pixels under one microlens record different directions.
So a 20 megapixel sensor with 10×10 angular samples gives a 0.2 megapixel image.
That is a 200,000-pixel photograph from a 20-million-pixel sensor — and consumers compare megapixels.
Later designs recovered some resolution by refocusing the microlenses, trading angular range instead. The trade moved; it did not disappear.
CSCE 748 · Computational Photography — Module 09
7

## Slide 9
PART 3
What you can compute
The payoff for capturing four dimensions.
CSCE 748 · Computational Photography — Module 09
8

## Slide 10
OPERATIONS
Rendering from a light field
▪ Refocusing: integrate over a sheared slice of the 4D function. Different shear, different focal plane.
▪ Synthetic aperture: integrate over a chosen subset of directions. A small subset gives deep focus; a large one gives shallow.
▪ Viewpoint change, within the capture aperture. Small parallax, computed for free.
▪ Depth estimation: the focal plane at which a region is sharpest gives its depth. Depth from one shot.
▪ Seeing through occluders: a synthetic aperture wider than the occluder integrates around it.
CSCE 748 · Computational Photography — Module 09
9
Notes: Seeing through foliage with a camera array is the most striking demo and is worth showing.

## Slide 11
Refocusing is a shear followed by an integral
THE CORE OPERATION
Reparameterising the two planes to a different separation is a shear of the 4D function.
Integrating the sheared function over the angular dimensions produces an image focused at the corresponding depth.
So refocusing is: shear, then sum. A few lines, once the light field is in hand.
And the Fourier slice theorem gives a faster route — a slice of the 4D Fourier transform is the transform of the 2D projection, so refocusing can be done in frequency space at lower cost.
CSCE 748 · Computational Photography — Module 09
10

## Slide 12
PART 4
What happened
An honest commercial post-mortem.
CSCE 748 · Computational Photography — Module 09
11

## Slide 13
Lytro failed, and the reasons are instructive
THE COMMERCIAL STORY
Resolution. A 1-megapixel output in an era of 12-megapixel phones. The headline feature cost the thing everyone compares.
The problem was not acute. Autofocus is good and getting better; photographers rarely wished they could refocus afterwards.
Depth from stereo and from learned monocular estimation arrived, giving portrait mode without the resolution cost.
And bokeh could be synthesised (Module 11) convincingly enough. The capability survived; the capture method did not.
CSCE 748 · Computational Photography — Module 09
12

## Slide 14
WHERE IT LIVES
Where light fields are actually used
Domain
Use
Microscopy
Single-shot volumetric capture of fast biological processes
Industrial inspection
Depth and surface detail in one shot
Film and VFX
Capture rigs for relighting and view synthesis
Research into displays
Light field displays may fix vergence-accommodation (CSCE 650)
Neural scene representations
NeRF and successors are light fields learned, not sampled
CSCE 748 · Computational Photography — Module 09
13
Notes: The NeRF connection is the live one — it is the same representation reached by a different route.

## Slide 15
Neural radiance fields are the idea, reached differently
WHERE THIS WENT
A NeRF represents a scene as a function from position and direction to radiance — which is the plenoptic function, learned rather than sampled.
Instead of capturing the 4D function densely, fit a network to a sparse set of photographs and query it anywhere.
This solves the sampling problem that made light field capture impractical — you no longer need every ray, only enough to constrain the fit.
And it inherits the question of Module 13: the rendered novel views are inferred, not measured, and the distinction matters.
CSCE 748 · Computational Photography — Module 09
14

## Slide 16
What to carry forward
1. The plenoptic function has seven dimensions; radiance invariance in free space reduces it to a 4D light field — the same fact that made ray tracing a lookup.
2. A conventional photograph is a 2D slice: the aperture integral destroys angular information irreversibly at capture.
3. A plenoptic camera trades spatial resolution for angular — a 20 MP sensor with 10×10 angular samples yields 0.2 MP.
4. Refocusing is a shear of the 4D function followed by an integral, and the Fourier slice theorem gives a faster route.
5. Lytro failed on resolution against a problem that was not acute, and depth estimation plus synthetic bokeh delivered the capability without the cost.
6. The representation survives in microscopy, VFX, light field displays, and — learned rather than sampled — in NeRF.
CSCE 748 · Computational Photography — Module 09
15