## Slide 1
UNIVERSITY OF CLAUDE
CSCE 640 — Quantum Algorithms
MODULE 11
Near-Term Hardware
What the current generation can and cannot be expected to do.
CSCE 640 · Module 11 of 13 · original material, share freely

## Slide 2
MODULE OUTCOMES
What you will be able to do
▪ Describe the current hardware landscape and its limits.
▪ Explain variational algorithms and their appeal.
▪ State the barren plateau problem.
▪ Explain the input and output problems.
▪ Assess a near-term application proposal.
CSCE 640 · Quantum Algorithms — Module 11
1
Notes: State the outcomes before the content. Every slide that follows exists to serve one of these.

## Slide 3
PART 1
What exists
Stated carefully, because it dates quickly.
CSCE 640 · Quantum Algorithms — Module 11
2

## Slide 4
Current devices have tens to hundreds of physical qubits, error rates near the threshold, and no useful error correction
THE LANDSCAPE, AS OF THIS COURSE'S WRITING
Superconducting, trapped-ion, neutral-atom, and photonic platforms all exist, with different trade-offs between gate speed, coherence time, and connectivity (Module 04 §3's tension).
Two-qubit gate error rates are around a fraction of a percent on the best systems — which bounds useful circuit depth to hundreds of gates, not millions.
And connectivity is limited: a circuit assuming all-to-all coupling must be compiled with swap networks, which multiplies the gate count.
So the honest statement is: these are real quantum devices and they are not fault-tolerant computers — Preskill's NISQ term names exactly this gap, and the gap is the subject of this module.
CSCE 640 · Quantum Algorithms — Module 11
3

## Slide 5
PART 2
Variational algorithms
The near-term hope, and its structure.
CSCE 640 · Quantum Algorithms — Module 11
4

## Slide 6
VARIATIONAL
The hybrid loop
text
THE IDEA
keep the quantum circuit shallow, and let a
classical optimiser do the hard work.
THE LOOP
1 prepare a parameterised state |psi(theta)>
with a short circuit
2 measure an expectation value, e.g. the
energy of a Hamiltonian
3 a CLASSICAL optimiser proposes new theta
4 repeat until converged
INSTANCES
VQE chemistry ground states (M09)
QAOA combinatorial optimisation
WHY IT APPEALS
shallow circuits fit inside the coherence time
and some errors are absorbed by reoptimising
the parameters
WHY IT IS DIFFICULT
see Part 3: the optimisation landscape
Shallow circuit, classical optimiser — which fits the hardware, and moves the difficulty into the optimisation.
CSCE 640 · Quantum Algorithms — Module 11
5

## Slide 7
PART 3
Barren plateaus
The obstacle, and it is structural.
CSCE 640 · Quantum Algorithms — Module 11
6

## Slide 8
For random parameterised circuits, gradients vanish exponentially in the number of qubits
WHY THE OPTIMISATION IS THE HARD PART
The expected gradient of the cost is zero and its variance shrinks exponentially with qubit count — so the landscape is flat almost everywhere, and the optimiser has nothing to follow.
Which means the number of measurements needed to resolve a gradient grows exponentially — exactly the scaling the method was supposed to avoid.
And it is not a tuning problem — it is a property of expressive random circuits, and more expressive ansätze make it worse, which is an uncomfortable trade.
So the mitigations all restrict expressiveness — problem-informed ansätze, shallow local cost functions, layerwise training — and restricting expressiveness is in tension with capturing the physics, which is the field's open question.
CSCE 640 · Quantum Algorithms — Module 11
7

## Slide 9
PART 4
Input and output
The two problems that undermine most proposals.
CSCE 640 · Quantum Algorithms — Module 11
8

## Slide 10
THE CAVEATS
What to check in any near-term application proposal
▪ The input problem — loading a classical dataset of size N into amplitudes generally costs O(N), which destroys a polynomial advantage before the algorithm starts (Module 07 §3).
▪ The output problem — the result is a quantum state, and extracting more than a few numbers from it costs exponentially many measurements (Module 02 §2).
▪ The classical baseline — which must be the best known method, and frequently is not checked (Module 13 §3).
▪ The assumed hardware — error rate, connectivity, and whether error correction is assumed, all three stated.
▪ And the scaling claim — asserted asymptotically, or measured over a range? Usually the former, on a range too short to fit.
Input and output together eliminate most proposed quantum machine learning applications — which is a strong claim and is the one the careful papers make.
CSCE 640 · Quantum Algorithms — Module 11
9

## Slide 11
And the honest near-term position
CLOSING
No convincing demonstration of a near-term quantum advantage on a useful problem has been made, as of this course's writing — which is a factual statement rather than a prediction.
And the sampling demonstrations are real results — a device sampling from a distribution classical simulation struggles with — on problems chosen to be hard to simulate rather than useful, which is the point and is sometimes lost.
Several of those have been substantially reduced by improved classical simulation afterwards (Module 13 §3) — which is science working, not scandal.
So the near-term honest answer to 'what can a hundred noisy qubits do' is: physics experiments, benchmarks, and algorithm development — which is a reasonable thing for a technology at this stage to be.
CSCE 640 · Quantum Algorithms — Module 11
10

## Slide 12
What to carry forward
1. Current devices are real quantum devices and are not fault-tolerant computers; NISQ names exactly that gap.
2. Two-qubit error rates near a fraction of a percent bound useful circuit depth to hundreds of gates.
3. Variational methods keep the circuit shallow and move the difficulty into a classical optimiser.
4. Barren plateaus: gradients vanish exponentially in qubit count, so the measurements needed grow exponentially.
5. Mitigations restrict expressiveness, which is in tension with capturing the physics.
6. Input and output costs together eliminate most proposed quantum machine learning applications.
CSCE 640 · Quantum Algorithms — Module 11
11